## Slide 1
WATER-ENERGY
NEXUS
HEJC, 16TH FEBRUARY 2018
CARLO A. AMADEI
Notes: PREMISE it is usually food energy water geographically dependent and also land use city vs rural

## Slide 2
WATER IS NEEDED FOR FOOD PRODUCTION
FOOD PRODUCTION AFFECTS WATER AVAILABILITY
ENERGY IS NEEDED FOR FOOD
PRODUCTION
ENERGY CAN BE
PRODUCED FROM
FOOD
WATER IS NEEDED FOR ENERGY PRODUCITON
ENERGY IS NEEDED FOR MOVING AND TREATINF WATER

## Slide 3
WATER IS NEEDED FOR FOOD PRODUCTION
FOOD PRODUCTION AFFECTS WATER AVAILABILITY
ENERGY IS NEEDED FOR FOOD
PRODUCTION
ENERGY CAN BE
PRODUCED FROM
FOOD
WATER IS NEEDED FOR ENERGY PRODUCITON
ENERGY IS NEEDED FOR MOVING AND TREATING WATER

## Slide 4
HIGH SPATIAL VARIABILITY
http://berc.berkeley.edu/wp-content/uploads/2013/06/Saxum_Energy_Final-Front.jpg

## Slide 5
http://www.wrcc.dri.edu/precip.html
HIGH SPATIAL VARIABILITY
Notes: -rainforest > 70 inches per year
WEST: We have low pressure stream coming from the pacific. Where you have warm moisture water that raises and condense…Orographic lifting
SW lack of water of evaporation
SE humid area affected by warme humid air coming from the Gulf
NE: coming from the Ocean, also coming down from Canada
LET S HOW THEY INTERACT IN REAL

## Slide 6
DOE, 2014
INTERSECTION
Notes: It is as complicated as interesting diagram express in quadrillion BTU and Billion gallon day
In the energy space:
circa 80% of our energy coming from fossil fuel (83/96) the remaining is evenly split between nuclear and renewable
1/3 1/3 1/3 in industrial, transportation, residential and commercial
Overall circa 1/3 efficiency,
In the water space:
exploitation of fresh water
Fresh ground water mainly consumed by agriculture
Regarding the intersection:
Residential/industrial/commercial and above all electricity generation
Primary energy used
Italy 1800 TWhy
US 27000 TWhy
Electricity consumed
US 4TWhy
Italy 300 Gwhy
Let’s have a look at the water withdrawals

## Slide 7
US WATER WITHDRAWALS: circa 350 BGD
USGS, 2010
78%
22%
16%
84%
Ground
Surface
Fresh
Saline
Notes: These are withdrawals which is different from consumption
Consumption: taken out form the cycle
Withdrawals: if it is quality is degraded (thermal pollution (20-25 F), decrease in Oxygen content, use water in air pollution control technology for ash removal or wet scrubber)

## Slide 8
BARCLAYS, 2017

## Slide 9
i)SURFACE WATER and GROUNDWATER
ii) OCEAN
iii) DRINKING/TREATED WATER (urban)
iv) WASTEWATER

## Slide 10
SURFACE WATER: Withdrawn or consumed to produce energy
Withdraw: 140 BGD (40% of the total withdraw)
Consumption: 4 BGD
DOE, 2014
Notes: Main difference is between close and open loop
Open: adv: water temp is constant disad:you need to be close to a large body and you need to clean the water
Close: recirculating and the fluid cooled by the air. Adv Require less water withdrawals disad: affect by outside temp, high capital inv
thermoelectric power plants alone contribute 50 percent to 60 percent of all toxic pollutants discharged to surface waters by all industrial categories under the Clean Water Act
Water is consumed when it is removed completely from the system, such as by evaporation or consumption by crops or humans.
withdrawal’ is defined as the amount of water removed from the ground or diverted from a water source for use, while ‘consumption’ refers to the amount of water that is evaporated, transpired, incorporated into products or crops, or otherwise removed from the immediate water environment

## Slide 11
SURFACE WATER: Withdrawn or consumed to produce energy
Withdraw: 140 BGD (40% of the total withdraw)
Consumption: 4 BGD
DOE, 2014
Notes: Main difference is between close and open loop
Open: adv: water temp is constant disad:you need to be close to a large body and you need to clean the water
Close: recirculating and the fluid cooled by the air. Adv Require less water withdrawals disad: affect by outside temp, high capital inv
thermoelectric power plants alone contribute 50 percent to 60 percent of all toxic pollutants discharged to surface waters by all industrial categories under the Clean Water Act
Water is consumed when it is removed completely from the system, such as by evaporation or consumption by crops or humans.
withdrawal’ is defined as the amount of water removed from the ground or diverted from a water source for use, while ‘consumption’ refers to the amount of water that is evaporated, transpired, incorporated into products or crops, or otherwise removed from the immediate water environment

## Slide 12
MACKNICK, 2012

## Slide 13
MACKINCK, 2012

## Slide 14
INFINITE COOLING

## Slide 15
GROUND WATER: polluted to produce energy?
HOWELL, 2017
ENGELDER, 2011
CONCERNS on the FRACKING FLUID
Notes: 2-10 MIL gallon of water each horizontal well
So if it is 1% 100k gallon of acid, biocide, surfctant (so almost half of Olympic pool)
Formation chemical: radionuclides, toxic metal
Introduced chemicals: reduce fouling, surfactants, hydrochloric acid to dissolve limestone
low pH to etch certain rock, friction reducer
You could reuse the water but high concentration of scaling Ca, Fe, Mg, Mn, and Sr
3 fluids
Fracking fluids
Natural brine
NG (methane and longer chain hydrocarbons)

## Slide 16
.
RISK = toxicity * exposure:
POOR WELL CONSTRUCTION
SPILLS of WASTEWATER
CONFINMENT of FRACKING FLUID
GROUND WATER: polluted to produce energy?
Notes: describes data gaps and uncertainties that limited our abilities to draw additional conclusions
Data sharing can promote understanding and trust among stakeholders—but technical and nontechnical barriers around data must be surmounted. Water-quality investigators must follow the path that academic and USGS seismologists have fol-lowed by agreeing on standards for mea-suring and reporting

## Slide 17
i)SURFACE WATER and GROUNDWATER
ii) OCEAN
iii) DRINKING/TREATED WATER (urban)
iv)WASTEWATER

## Slide 18
OCEAN: cooling (today), energy production (future)
SURFACE ACTUTOR
POINT SOURCE BUOY
TIDAL BARRIAGE
Notes: DOE, in collaboration with researcher from Georgia Tech, mapped and quantified the availability of tidal power in then US.
The reports find that tidal energy could produce 1410 TWhy (5% of the electricity supply)
150 Gw

## Slide 19
DOE, 2014
INTERSECTION

## Slide 20
i)SURFACE WATER and GROUNDWATER
ii) OCEAN
iii) DRINKING/TREATED WATER (urban)
iv)WASTEWATER

## Slide 21
TREATING DRINKING WATER: sink of energy
i) Pumping groundwater/surface water
ii) Desalination
ii) Wastewater reclamation
REMILLARD, 2018

## Slide 22
i) PUMPING GROUND/SURFACE WATER: 0.25-4 kWh/m3
Highly dependent on where the water is coming from:
Groundwater (rural)/surface water (urban) rural/city
Distance
52 billion kWh
State Water Project (California):
3.3 kWh/m3 S.Cal
1 kWh/m3 N.Cal
California aqueduct (400 miles, >300 m3/s)
New York
.5-.7 kWh/m3 due to gravity-fed distribution
ESMAP,2012
Notes: 52 bil kwh about 150 W per person.
US citizen in electricity 1.5 kWh. So 10% of the electricity is spent in pumping and supplying water.
Apart form pumping energy is spent in coagulaiton, flocculation, sedimenation, and chlorination
California in track to have 1/3 of its electricity from renewable.

## Slide 23
ii) DESALINATION: 3-5 kWh/m3
ELIMELECH,2011
Carlsbad Desalination plant
State of the art
Largest in the wester hemisphere
Baseline design: 3.9kWh/m3
10% San Diego DW
Notes: >1 kWh/m3 , is consumed by the intake, pretreatment, posttreatment, and brine discharge stages of the desalination plant (4). Of these stages>1 kWh/m3 , is consumed by the intake, pretreatment, posttreatment, and brine discharge stages of the desalination plant (4). Of these stages
o the theoretical minimum energy required for desalination of 35 g/liter seawater at 50% recovery (1.06 kWh/m3 ). The energy data presented exclude the energy required for intake, pretreatment, posttreatment, and brine discharg

## Slide 24
i)SURFACE WATER and GROUNDWATER
ii) OCEAN
iii) DRINKING/TREATED WATER (urban)
iv)WASTEWATER

## Slide 25
iii) WASTEWATER RECLAMATION: 2-3 kWh/m3
0.25-1 kWh/m3 are already used for primary and secondary treatment
AMADEI, 2016

## Slide 26
iii) WASTEWATER RECLAMATION: 2-3 kWh/m3
0.25-1 kWh/m3 are already used for primary and secondary treatment
AMADEI, 2016
WW contains almost 10 times the energy needed to treat it

## Slide 27
iii) WASTEWATER RECLAMATION: up to 9 kWh/m3 in energy recovery (paradigm shift)
Notes: Maximize energy and water recovery.
Reover nutrients
41,900MJ/m3 of wastewater is possible for every 10 1C temperature difference
The chemical energy ranges between 12 and 15 MJ/kg of COD (organics) and between 27.4 and 29.4 MJ/kg
t was estimated that wastewater contains 9.3 times the energy required to treat it
9.8 kJ/m3 per m of head for water

## Slide 28
waste-to-fuel; organics → 70% CH4 30% CO2;
0.5 kgCOD m-3 WW; 0.16 kgTOC m-3 WW
1.9 kWh m-3 WW
2) nutrient recycling; (N-NH3, P-phosphate)
40 gN & 8 gP m-3 WW; Haber-Bosch 7% elec.
0.8 kWh m-3 WW 150,000,000 tons fertilizer
3) heat recovery; (6oC)
7.0 kWh m-3 WW
McCarty PL et al., Environ. Sci. Tech., 2011.
iii) WASTEWATER RECLAMATION: up to 9 kWh/m3 in energy recovery (paradigm shift)
Notes: Habor Bosh to produce ammonia and it requires high temp
Three to five percent of the world's natural gas production is consumed in the Haber process (around 1–2% of the world's annual energy supply

## Slide 29
WATER-ENERGY
NEXUS
Notes: PREMISE it is usually food energy water geographically dependent and also land use city vs rural

## Slide 30: REFERENCES
The water-energy nexus (DOE,2014)
Total Water Use in the United States, 2010 (USGS,2010)
The water challenge: preserving a global resource (Barclays, 2017)
Operational water consumption and withdrawal factors for electricity generating technologies: a review of existing literature (Macknick, 2012)
The water consumption of energy production: an international comparison (Spang, 2014)
How do U.S. state residents form opinions about ‘fracking’ in social contexts? A multilevel analysis (Howell, 2017)
Should fracking stop? (Engelder, 2011)
The Future of Seawater Desalination: Energy, Technology, and the Environment (Elimelech, 2011)
PhD defense (Remillard,2018)
Hydraulic “Fracking”: Are Surface Water Impacts An Ecological Concern? (Burton, 2014)
The truth about fracking (Mooney, 2011)
Energy and water autarky of wastewater treatment and power generation systems (Gude, 2015)

## Slide 31
Back-up slides

## Slide 33
SPANG, 2014
Water consumption for various electricity generation
Notes: ST = steam turbine; CC = combined cycle; GT = gas turbine; PV = photovoltaic; NA = not applicable. Thermoelectric cooling technologies: CT = cooling tower; OTF = once-through freshwater; CP = cooling pond; AIR = dry cooling.

## Slide 34
BURTON, 2014

## Slide 35: Water in thermopower plant - thermal pollution (20-25 F) - decrease in Oxygen content - use in air pollution control technology for ash removal or wet scrubber -Acid mine drainage for coal According to the EPA, thermoelectric power plants alone contribute 50 percent to 60 percent of all toxic pollutants discharged to surface waters by all industrial categories under the Clean Water Act Clean Water Act (CWA), to “restore and maintain the chemical, physical, and biological integrity of the Nation's water

## Slide 36: Cali report 2016

## Slide 37
DATA
the EU for example, energy production accounts for 44 percent of total water use. Conversely, energy is also needed to process water for consumption. By 2050, the global population will demand roughly 80 percentmore energy and 55 percent more water than today
IRENA analysis finds that doubling the share of renewable energy, in particular solar PV and wind, could reduce water withdrawals in the power sector as much as 52 percent in the UK, 37 percent in the US, 32 percent in Australia, 28 percent in Germany and 12 percent in India

## Slide 38
DATA
DOE‘s integrated strategy for addressing challenges across the water-energy nexus rests on six pillars:
 Optimize the freshwater efficiency of energy production, electricity generation, and end use systems
 Optimize the energy efficiency of water management, treatment, distribution, and end use systems
 Enhance the reliability and resilience of energy and water systems
 Increase safe and productive use of nontraditional water sources
 Promote responsible energy operations with respect to water quality, ecosystem, and seismic impacts
 Exploit productive synergies among water and energy systems