## Slide 1: Energy End-uses: Residential and Commercial Sectors
Rupak Chakraborty
HEJC
November 19, 2015

## Slide 2: Global energy end-use
IEA 2013
40 PWh

## Slide 3: What is in “Other”?
IEA 2013
Notes: 2010 numbers:
24% for residential
8% for commercial
32% total

## Slide 4: Buildings
32% of global final energy end use; 19% of all global GHG emissions
Fossil fuel combustion
Electricity use
IPCC WG3 AR5
Notes: Most comes from indirect CO2 emissions from electricity use in buildings
Indirect emissions are growing faster than direct emissions

## Slide 5: Regional emissions growth
IPCC WG3 AR5
Notes: Growth driven by non-OECD Asia, no surprisingly

## Slide 6: End-use breakdown
IPCC WG3 AR5
Notes: World building final energy consumption be end-use in 2010
Most of this is thermal energy use – cooking, space heating, water heating
Cooling, suprisingly, is only a small fraction of the total energy use in these sectors

## Slide 7: Reduction potentials
IPCC WG3 AR5

## Slide 8: Thermal improvements: new buildings
New buildings
  Passive House Standard: 15 kWh/m2/yr for heating (60-250 typical)
Notes: As discussed in
AR4, essential steps in the design of low-energy buildings are:
(1)
building orientation, thermal mass, and shape;
(2) high-performance
envelope specification;
(3) maximization of passive features (day-
lighting, heating, cooling, and ventilation);
(4) efficient systems meet-
ing remaining loads;
(5) highest possible efficiencies and adequate
sizing of individual energy-using devices; and
(6) proper commission-
ing of systems and devices.

## Slide 9: Thermal improvements: old buildings
Comprehensive retrofits can result in 50-75% reduction
Modest insulation upgrades in developing countries can achieve reduction in heating energy by 66%

## Slide 10: Thermal improvements: decentralized cooling
Beijing, China
IPCC WG3 AR5

## Slide 11: Thermal improvements: decentralized cooling
Philadelphia
IPCC WG3 AR5

## Slide 12: Cooking
50 % savings potential just through changing cooking practices
Oberascher et al. 2011

## Slide 13: Efficiency aligned with economics?
Up-front cost
Lack of information
Principal-agent problem
Inaccurate discount rate
Unintended behavioral changes
McKinsey 2010
Why aren’t these happening more frequently?
Notes: -often it is the rational economic choice to be energy efficient, but people discount
Lack of information:
Existence of efficient appliances or knowledge of potential savings not known
Principal agent problem
Apartment complex
Inaccurate discount rate
CAFÉ standards just make clear to the consumer
Unintended behavioral changes

## Slide 14: Reduction potentials

## Slide 15: Reduction potentials
2°C less
Shorter showers
Fans
Cooking practices
Turning off
No beer fridge
Fully loaded
Wash cold
Full load; air dry

## Slide 16: How the digital world helps
Consumption data visibility (smart meters)
Automated hardware
  Smart thermostats/vents

## Slide 17: Behavioral changes…for the better
Enabled by…data utilities already had

## Slide 18: Retrofit decentralized cooling
Smart vents (Keen Home, Ecovent)

## Slide 19: Retrofit smart thermostats: Nest

## Slide 20: Retrofit smart thermostats: Nest

## Slide 21: Smart meters
Smart meters record energy consumption at < 1hr intervals
Enables real-time tracking of consumption, enabling demand management

## Slide 22: Peak demand => dirty fuels and higher price

## Slide 23: Smart meters enable demand-management
OhmConnect: notifies you during peak hours, and you get paid to turn down your AC/heat
ENERNOC and others: same for industry

## Slide 24: Summary
19% of global GHG emission due to residential and commercial building use
Recent growth largely due to rising electricity consumption
Most energy use at residential and commercial level is for thermal energy
Economic incentives may align with energy efficiency, but detrimental behavioral changes must be thought through
Behavioral change is a key mitigation strategy, enabled by
  Visibility into energy consumption
  Automation of energy usage

## Slide 25: Electricity consumption
IPCC WG3 AR5