## Slide 1: Vibrational Energy Harvesting
Eliza Kate Spear
HEJC
2020-11-20
Notes: Images from https://revibeenergy.com/

## Slide 2: Vibrational energy harvesting (VEH) converts vibrational energy to electrical energy
Vibrational energy is harvested using a transducer, which is a device that converts one form of energy to another (in this case, kinetic to electrical)

## Slide 3: VEH is an attractive option for wireless sensor networks (WSN)
Wireless sensors generally require batteries, but replacing those batteries can be challenging, expensive, and impractical.
VEH also finds application in medical devices, e.g. in pacemakers, where battery replacement necessitates surgery.
For some sensors, e.g. on industrial machinery or on bridges to monitor bridge health, vibrations in the sensor environment can provide enough energy to power the device.

## Slide 4: For sensors in the right environment, VEH can be a convenient choice
Wireless sensor networks have a host of energy options; specifics of the sensor environment will dictate whether VEH is appropriate.
Shaikh, F. K.; Zeadall, S. Renew. Sust. Energ. Rev. 2016, 55, 1041-1054.

## Slide 5: Sources of energy
Priya, S. et al. Energy Harvesting and Systems 2017, 4 (1), 3-39.

## Slide 6: Power density of ambient energy sources
https://www.intechopen.com/books/small-scale-energy-harvesting/electrostatic-conversion-for-vibration-energy-harvesting
Notes: https://www.intechopen.com/books/small-scale-energy-harvesting/electrostatic-conversion-for-vibration-energy-harvesting
DOI: 10.5772/51360

## Slide 7: Wireless sensor node power consumption
https://www.intechopen.com/books/small-scale-energy-harvesting/electrostatic-conversion-for-vibration-energy-harvesting
Notes: https://www.intechopen.com/books/small-scale-energy-harvesting/electrostatic-conversion-for-vibration-energy-harvesting
DOI: 10.5772/51360

## Slide 8: Sources of vibrational energy
Priya, S. et al. Energy Harvesting and Systems 2017, 4 (1), 3-39.
Considering a simple mass-spring-damper system, maximum power can be obtained from low frequency vibrations with high acceleration
(𝜁m is the mechanical damping factor)
Notes: https://faculty.washington.edu/seattle/physics227/reading/reading-3b.pdf

## Slide 9: Frequency and acceleration of vibration from various sources
Image Source: Siang, J.; Lim, M. H.; Salman Leong, M. Int. J. Energy Res. 2018, 42, 1866-1893.
Acceleration (m/s2)
Frequency (Hz)

## Slide 10
Electromagnetic
Piezoelectric
Electrostatic
Additional niche methods include magnetostrictive and flexoelectric
triboelectric
capacitive
Three Main Methods of VEH

## Slide 11: Electromagnetic VEH
General Concept: vibrating magnet generates current in a conductive coil
Advantages: simple construction, high conversion efficiency
Disadvantages: low voltage compared to piezoelectric and electrostatic VEH, difficult to scale down (micro- and nano-scale coils)
Image Source: Siang, J.; Lim, M. H.; Salman Leong, M. Int. J. Energy Res. 2018, 42, 1866-1893.

## Slide 12: Piezoelectric VEH
The piezoelectric effect is a material property, where mechanical strain induces an electric field in the material (conversely, in the reverse piezoelectric effect, an applied electric field induces deformation)
Image Source: Shaikh, F. K.; Zeadall, S. Renew. Sust. Energ. Rev. 2016, 55, 1041-1054.

## Slide 13: Piezoelectric VEH
The piezoelectric effect is a material property, where mechanical strain induces an electric field in the material
Zheng, Q. et al. Adv. Sci. 2017, 4, 1700029.
Example: the piezoelectric effect in ZnO

## Slide 14: Piezoelectric VEH
Priya, S. et al. Energy Harvesting and Systems 2017, 4 (1), 3-39.
Unimorph Structure
Cantilever-based piezoelectric harvester design
Mass (purple) adjusts resonant frequency to the available environmental frequency

## Slide 15: Piezoelectric VEH
General Concept: vibration induces a voltage across a piezoelectric material; typical piezoelectrics used are PZT (Pb(Zr,Ti)O3) and AlN
Advantages: simple construction, can be smaller than electromagnetic VEH
Disadvantages: lifespan issues due to brittleness, depolarization of the dielectric (especially in high temperature environments)
Image Source: Priya, S. et al. Energy Harvesting and Systems 2017, 4 (1), 3-39.
Cantilever-based piezoelectric harvester design

## Slide 16: Electrostatic VEH – capacitive
In-plane overlap type
In-plane gap closing type
Out-of-plane gap closing type
A capacitor, with two electrically isolated plates, is charged via an external voltage source. The electrostatic force between the plates is given by (constant charge) or (constant voltage). Vibration changes the distance between the plates (a,b) or the area of overlap (a), and the work done against the electrostatic force provides the harvested energy.
Beeby, S. P. et al. Meas. Sci. Technol., 2006, 17, R175-R195.

## Slide 17: Electrostatic VEH – capacitive
General Concept: vibration either changes distance between capacitor plates or changes capacitor area
Advantages: straightforward fabrication (similar to existing MEMS components)
Disadvantages: requires an external voltage source
Beeby, S. P. et al. Meas. Sci. Technol., 2006, 17, R175-R195.
Varpula, A. et al. Sci. Rep. 2014, 4, 6799.

## Slide 18: Electrostatic VEH – triboelectric
“Triboelectric effect”, Wikipedia, accessed 2020-11-19. https://en.wikipedia.org/wiki/Triboelectric_effect
The triboelectric effect is a type of contact electrification where materials become electrically charged after they are separated from another material (e.g. static electricity)

## Slide 19: Electrostatic VEH – triboelectric
Wang, Z. L. Mater. Today 2017, 20 (2), 74-82.
Two dielectrics are driven into physical contact; charges build up in the two dielectrics via the triboelectric effect (ii)
With additional cycles, further charges build up to saturation, and the resulting electrostatic field drives electrons to flow through the external load (iii)

## Slide 20: Electrostatic VEH – triboelectric
Siang, J.; Lim, M. H.; Salman Leong, M. Int. J. Energy Res. 2018, 42, 1866-1893.

## Slide 21: Electrostatic VEH – triboelectric
General Concept: vibration induces contact and charge build-up via the triboelectric effect
Advantages: more mechanically robust than piezoelectric VEH
Disadvantages: low durability; high moisture environments affect device performance
Siang, J.; Lim, M. H.; Salman Leong, M. Int. J. Energy Res. 2018, 42, 1866-1893.

## Slide 22
Electromagnetic
Piezoelectric
Electrostatic
triboelectric
capacitive
VEH Summary

## Slide 23: VEH Summary
Electromagnetic
Piezoelectric
Electrostatic
General Concept: vibrating magnet generates current in a conductive coil
Con: difficult to scale down to MEMS scale
General Concept: vibration induces a voltage across a piezoelectric material
Con: lifespan issues (depolarization, brittleness), temperature sensitivity
Capacitive
General Concept: vibration either changes distance between capacitor plates or changes capacitor area
Con: requires an external voltage source
Triboelectric
General Concept: vibration induces contact and charge build-up via the triboelectric effect
Con: lifespan issues, moisture sensitivity

## Slide 24: VEH Summary
Electromagnetic
Piezoelectric
Electrostatic
General Concept: vibrating magnet generates current in a conductive coil
Con: difficult to scale down to MEMS scale
General Concept: vibration induces a voltage across a piezoelectric material
Con: lifespan issues (depolarization, brittleness), temperature sensitivity
Capacitive
General Concept: vibration either changes distance between capacitor plates or changes capacitor area
Con: requires an external voltage source
Triboelectric
General Concept: vibration induces contact and charge build-up via the triboelectric effect
Con: lifespan issues, moisture sensitivity
Are any of these VEH systems commercially available?

## Slide 25
Appear to have commercial electromagnetic VEH products available!
From their website: “If you are looking into the Internet of Things and consider costly cable installations and battery replacements to be an issue, ReVibe’s energy harvesting solutions might just be the thing for you. If vibrations, impulses or other mechanical movement is found close to the applications that needs monitoring, we can offer you a sustainable, cost-efficient and completely autonomous power source!”
https://revibeenergy.com/

## Slide 26
https://revibeenergy.com/
Offer three standard VEH products and customized products
€645
€295
€695

## Slide 27
microGen Systems, Inc., founded 2010, was developing piezoelectric VEH; according to their LinkedIn page (probably last updated ~2011):
“microGen Systems, Inc., is the leading supplier of MEMS-based piezoelectric vibrational energy harvesting power generators and systems. We provide perpetual power solutions essential to the growth of the Internet of Things (IoT).”
Wireless Sensor Solutions, founded 2017, acquired microGen Systems (also in 2017):
https://www.linkedin.com/company/microgen-systems-inc/about/ and https://www.wsstec.com/
IIOT = industrial internet of things

## Slide 28: Questions?