## Slide 1: GeoMicroDistricts
Amos Meeks
Harvard Energy Journal Club
2/7/20

## Slide 2: There is a legal requirement to get off fossil fuels in the next 30 years.
2018 Natural Gas Use in MA
Chart: 
| Electric Power Consumers | Residential Consumption | Commercial Consumers | Industrial Consumption | Pipeline and Distribution Use
 | 133711 | 130296 | 118779 | 47524 | 8664
https://www.eia.gov/dnav/ng/NG_CONS_SUM_DCU_SMA_A.htm
Applied Economics Clinic Policy Brief, December 2019
Net Zero, 2050
Notes: Ability to balance heating and cooling loads over space and time, e.g. hocky rinks and grocery stores.

## Slide 3
Existing natural gas infrastructure is old and leaky

## Slide 5
Estimated cost to repair: $9,000,000,000

## Slide 6: Local nonprofit HEET commissioned a report to look at the idea of a GeoMicroDristrict
Notes: HEET Budget is less than $200,000 per year.

## Slide 7: GeoMicroDistricts promise clean, utility-scale building climate control
Notes: Caveats: Very preliminary study
Note: It would provide cooling in addition to heating! Very important as we transition from heating-dominated to cooling-dominated in the next 50 years.

## Slide 8: Heat pumps are just a reversible refrigeration cycle
http://tidewatermechanical.com/geothermal-heat-pumps/

## Slide 9: Ground provides nearly constant temperature all year
Benzaama, Mohammed-Hichem et al. (2018). Investigation of the thermal behavior of a combined geothermal system for cooling with regards to Algeria’s climate. Sustainable Cities and Society. 43. 10.1016/j.scs.2018.08.016.
Notes: GSHP wells are usually 100 to 500 ft. Trench wells may only be a couple of meters, which provides some benefit but not nearly as much

## Slide 10
Greatly reduced emissions
Increased Safety
Capture of waste heat
Notes: CO2 emissions only from materials and electricity
Safety
Facilitates use of waste heat from e.g. data centers, supermarkets, ice rinks, etc.

## Slide 11: Annual heating and cooling loads must be balanced
=

## Slide 12: Modeling was done with four prototypical street types

## Slide 13: Model suggests that GMDs can meet heating and cooling loads in all cases except high-density
Notes: Load met goes up for mixed use because of waste heat use.

## Slide 14: Installation costs vary but are ≈$10,000/ton
Notes: the rate of heat transfer that results in the freezing (*or melting) of 1 short ton (2,000 lb; 907 kg) of pure ice at 0 °C (32 °F) in 24 hours. A refrigeration ton is approximately equivalent to 12,000 BTU/h or 3.5 kW. $10,000/ton ~= $3,000/kW.

## Slide 15: Installation costs are dominated by borehole drilling

## Slide 16: Operating costs are driven by backup heating/cooling needed for load balancing

## Slide 17: Operating costs are comparable to natural gas heating
Cost to heat the average MA home with natural gas is about $1,000/year
https://www.mass.gov/info-details/household-heating-costs

## Slide 18: Total conversion costs are comparable to gas infrastructure maintenance costs
Conversion costs per building ≈$103-105
Number of buildings in MA ≈106
Total conversion cost ≈$109-1011
Gas system maintenance costs ≈$1010
Notes: Order 10^6 buildings in MA. Costs range from 10^3 to 10^5, so total cost range 10^9 to 10^11.

## Slide 19: System conversion could pay for itself with a reasonable carbon price
Eventual reduction by about a factor of 10
Heating emissions currently 20 MtCO2/yr -> Reduction of 18 MtCO2/yr
Assuming 40 year lifetime: 40 yrs* 18 MtCO2/yr = 720 MtCO2
Notes: Heating ~20 MTCO2/yr. Lifetime ~40 years, so 800 MTCO2. Lets say this reduces emissions by an order of magnitude, so about 720 MTCO2. Let’s say cost is about $10^10. That’s about $10^1/tCO2 -> Reasonable! Sugggests that carbon abatement alone could pay for the transition, even without accounting for the needed benefits of heating and cooling.

## Slide 20: GMD will be tested in MA in the next few years
Jan 3 2020: Eversource submitted a rate case to do three pilots over three years. Currently in review by the MA DEP, up to 8 months.
Legislation recently passed by the state senate would specifically authorize utilities to pursue this.

## Slide 21: Conclusions
Initial feasibility study suggest that the GeoMicroDistrict is a potential low-emission way to provide building climate control for reasonable cost
Questions
How to provide carbon-free heating and cooling for high-density urban centers?
How should implementation be staged and incentivized?
How to get private building owners to change (energy efficiency upgrades + heat pump installation)?