## Slide 1: Overcoming the photovoltaic efficiency limit
Dr. Michael Purdy
Postdoctoral research fellow
Liu group

## Slide 2: Fossil fuels
Fossil fuels sources dwindling
Fossil fuels are accessible and cheap
Renewable energy technologies need to be economically competitive

## Slide 3: Photovoltaics
Semiconductor technology that converts solar energy into electrical energy
40 % annual growth in global photovoltaic capacity from 2000-2015
Highest performing Si-based PV device currently has an efficiency of 26.5 %

## Slide 4: How photovoltaics work

## Slide 5: Shockley - Queisser limit
Efficiency of PV devices cannot exceed 29%
Majority of energy lost via thermalisation
Overcoming thermalisation losses could lead to an efficiency increase to 40 %
Rao, A.; Friend, R. H. Harnessing Singlet Exciton Fission To Break the Break the Shockley-Queisser Limit. Nat. Rev. Mat. 2017, 2, 17063

## Slide 6: Thermalisation losses
Excess energy from > 1.1 eV photon lost via vibration decay
How can we overcome these losses and utilise higher energy photons?
Conduction band
Valence band
Thermalisation losses

## Slide 7: Singlet fission
Excited state electron multiplication process
Triplets > 1.1 eV could be harnessed by silicon
Use a singlet fission organic chromophore to on top of silicon to harvest higher energy photons

## Slide 8: Singlet fission solar cell
Organic – inorganic exciton transfer is difficult
Quantum dots accept the triplet

## Slide 9: Photon multiplier technology
Currently being developed at University of Cambridge
Research led by Professor Hugo Bronstein and Professor Akshay Rao

## Slide 10: Limitations to technology
Strict energetic requirements 2E(T1) < E(S1)
E(T1) > 1.1 eV
Solid state interactions tuned
Stability

## Slide 11: Current materials
No organic material yet satisfies all the requirements

## Slide 12: Nearly there
Energy level alignment 
Triplet energy ~ 1.1 eV 
Photostability
Purdy, M. et al. Aza-Cibalackrot: Turning on Singlet Fission Through Crystal Engineering. J. Am. Chem. Soc. 145, 10712–10720 (2023)

## Slide 13: Beyond singlet fission
Multijunction cells
Light concentration
Photon upconversion
Purely organic solar cells

## Slide 14: Multijunction cells
A series of photovoltaic cells that absorb different photon energies
Take full advantage of the solar spectrum
Three layers can reach 48 %
Very expensive

## Slide 15: Light concentration
Intensity of 1.1 eV photons can be concentrated using mirrors
Can lead to overheating which can reduce efficiency
Efficiency could be raised to 37 %

## Slide 16: Photon upconversion
Opposite to singlet fission
Two low energy photons that can’t be utilised by PV are combined
No device has been developed yet

## Slide 17: Purely organic solar cells
Alternative strategy is too remove silicon and only use organics
Plastic solar cells been manufactured

## Slide 18: How they work

## Slide 19: Advantages over silicon
Flexible and cheap
Solar windows
Conductive paint
Strong light absorbers

## Slide 20: Disadvantages
Maximum efficiency ~ 20 %
Less easily transport charges

## Slide 21: Conclusions
Silicon is a robust and reliable photovoltaic material
Efficiency limit must be overcome in an economically sustainable way
Organic solar cells show potential for future application