## Slide 1: Electrification of Ammonia Synthesis for Sustainability
Kindle Williams
Manthiram Lab
Harvard Energy Journal Club
16 October 2020

## Slide 2: Chemical manufacturing represents a large carbon footprint
Z. J. Schiffer and K. Manthiram Joule 1 10-14 (2017).
Chemical industry emits 7% of global GHG emissions
Ammonia alone represents >1% of global GHG emissions
Notes: Difficult to decarbonize because sometimes the emissions are associated with the chemistry of the process.

## Slide 3: This ammonia is mostly used in fertilizers
Scheme: Nik Lazouski

## Slide 4: Fertilizers support the global population

## Slide 5: The current process: Haber-Bosch
Ahmad, S. ud D. 2015
1.9-9 ton CO2/ton NH3
>450 million tons CO2/yr
Only economically viable at large scales
  ~3000 ton/day
Centralized production
Large capital cost
  $1B+ per plant
Out of reach for many less-wealthy economies

## Slide 6: Two components: H2 production and ammonia synthesis
1: Hydrogen Production
2: Ammonia Synthesis
“Colors” of H2:
  Grey
  Blue
  Green
  Turquoise
Haber-Bosch
Plasma-based approaches
Electrochemical approaches
scale match
Notes: Note: almost half of industrially produced H2 goes to ammonia synthesis.

## Slide 7: Two components: H2 production and ammonia synthesis
1: Hydrogen Production
2: Ammonia Synthesis
“Colors” of H2:
  Grey
  Blue
  Green
  Turquoise
Haber-Bosch
Plasma-based approaches
Electrochemical approaches
scale match
Notes: Note: almost half of industrially produced H2 goes to ammonia synthesis.

## Slide 8: Hydrogen production: “colors”
“Colors” of H2:
  Grey/Brown
Steam-methane reforming
Methane partial oxidation/ATR
Coal gasification
Water-gas Shift
Notes: SMR: Ni catalyst, endothermic, 14-40 bar, 800-900 C
WGS: exothermic
ATR = autothermal reforming
Technically coal is brown hydrogen
50% SMR, 30% oil, 20% coal today

## Slide 9: Hydrogen production: “colors”
“Colors” of H2:
  Grey/Brown
  Blue (Grey/Brown + CCUS)
Steam-methane reforming
Methane partial oxidation/ATR
Coal gasification
Water-gas Shift
Image: 2B1st Consulting

## Slide 10: Hydrogen production: “colors”
“Colors” of H2:
  Grey/Brown
  Blue
  Green
Image: AleaSoft
AEC (basic)
PEM (acidic)
SOEC (high-T)
  Mature w/ limitations
  Up-&-coming; promising
  Efficient, but research phase
  Note: other “green” methods that don’t involve electrolysis:
  PEC
  Photobiological
  High-T water splitting (concentrated solar/nuclear)
  H2O  H2 + ½ O2
Notes: Alkaline electrolysis cell
Proton exchange membrane
Solid oxide electrolysis cell
https://www.nrel.gov/docs/fy10osti/72740.pdf

## Slide 11: Hydrogen production: “colors”
“Colors” of H2:
  Grey/Brown
  Blue
  Green
  Turquoise (i.e. “blue-green”)
Images: Monolith Materials

## Slide 12: Two components: H2 production and ammonia synthesis
1: Hydrogen Production
2: Ammonia Synthesis
“Colors” of H2:
  Grey
  Blue
  Green
  Turquoise
Haber-Bosch
Plasma-based approaches
Electrochemical approaches
scale match
Notes: Note: almost half of industrially produced H2 goes to ammonia synthesis.

## Slide 13: Ammonia synthesis: thermodynamics & kinetics
Thermochemical
Conversion
X
Higher pressures to achieve reasonable conversions
X <20%
Higher temperatures to achieve reasonable rates
1/2 N2 + 3/2 H2  NH3
Electrochemical
At ambient pressure (1 atm):
X
Voltage also improves kinetics, so can operate at lower temperature
Apply voltage to increase conversion
X > 99%
Z. J. Schiffer and K. Manthiram Joule 1 10-14 (2017).
Hard to break the N2 triple bond

## Slide 14: Ammonia synthesis reactors: from industrial scale to leading-edge research
Commercial:
  Haber-Bosch
    100+ bar, 400-500 °C
    15% single-pass conversion, 97% overall conversion
    Iron oxide catalyst is easily poisoned
Image: BASF

## Slide 15: Ammonia synthesis reactors: from industrial scale to leading-edge research
Commercial:
  Haber-Bosch
Research-stage:
  Low-T/P Haber-Bosch
    Using Ruthenium catalyst, can:
    Improve kinetics  Lower-T operation  Lower-P operation  Decrease safety risk & lower capital cost

## Slide 16: Ammonia synthesis reactors: from industrial scale to leading-edge research
Commercial:
  Haber-Bosch
Research-stage:
  Low-T/P Haber-Bosch
  Plasma synthesis
    Thermal & non-thermal plasmas
    Low (~1%) efficiency because kV input required
Whitehead, J.C. Front. Chem. Sci. Eng. 13, 264–273 (2019).
Plasma generates radicals, which couple on a catalyst
Peng et al., J. Clean. Prod. 177, 597-609 (2018)
Notes: https://www.sciencedirect.com/science/article/pii/S0959652617332195?via%3Dihub

## Slide 17: Ammonia synthesis reactors: from industrial scale to leading-edge research
Commercial:
  Haber-Bosch
Research-stage:
  Low-T/P Haber-Bosch
  Plasma synthesis
  Electrochemical
Aqueous:
N2 + 3H2O  2NH3 + 3/2 O2
Generally pretty low-rate, hard to reproduce reports right now
Non-aqueous, Lithium-mediated:

## Slide 18: State-of-the-art vs. what is possible in the near-term
Replace the steam methane reforming/WGS with electrolyzers; add air separation; scale down H-B to match electrolyzer scale.
Smith et al., Energy Environ. Sci., 2020, 13, 331

## Slide 19: Generations of ammonia production technology

## Slide 20: The bigger picture: how does this fit into existing markets/regulations?
Markets:
  Agriculture (established, most of NH3 today)
    Traditional
    Greenhouse
    Urban
    Organic
  Chemical synthesis (e.g. nylon)
  Refrigerants
  Energy storage (growth potential)
Regulations
  Organic certification?
Chart: 
| Fertilizer | Chemical | Refrigeration | Fibers and plastics | Pharmaceuticals | Pulp and Paper | Other
 | 30.5405 | 5.9459 | 4.8649 | 2.973 | 2.1622 | 1.8919 | 1.0811
Fertilizers
Chemicals
Refrigeration

## Slide 21: What are folks doing today? Startups:
Nitricity
Starfire Energy
Producing NH3 at small scales
Low pressure operation – higher recycling costs, but cheaper capital than H-B
Targeting NH3 as fuel – low margin, high product; long approach to target market
Producing nitrate fertilizers at small scales
Plasma-based process: lower capital costs, high operating costs
Targeting off-grid production of fertilizer – need to pay off solar installations
*Disclaimer: this is not exhaustive!!*

## Slide 22: What are folks doing today? Big players:
*Disclaimer: this is not exhaustive!!*

## Slide 23: How does this fit into the big picture of sustainability?
Nitrogen cycle
  Inherent N losses to soil during fertilization
  N oxides are also greenhouse gases
Distributed fert. production could help with slower fert. application
  Less runoff

## Slide 24: Acknowledgements
Manthiram Lab
PI: Prof. Karthish Manthiram
Research/many slides: Nik Lazouski 
15.366 Climate & Energy Ventures
Contact me:
Kindle Williams
kindlew@mit.edu
Thanks for listening!

## Slide 25: References
Smith et al., Energy Environ. Sci., 2020, 13, 331: https://pubs.rsc.org/en/content/articlelanding/2020/ee/c9ee02873k
Lazouski et al., Nature Catal., 2020, 3, 463-469: https://www.nature.com/articles/s41929-020-0455-8

## Slide 26: Nitrogen production comparison (slide: Nik Lazouski)
Nitrogen is produced from air when fuels burn
Three methods of air separation
  Cryogenic
    Large production scales
    Energy intensive
    Produces very pure N2
    Not intermittent
  Pressure swing absorption
    Can produce high purity N2 (99.99%)
    Lower flowrates
  Membrane separations
    Only good for moderate purity (97-99% N2)
    Can get high flowrates
    Needs a large pressure drop
    Scales poorly with size
Notes: https://www.airbestpractices.com/system-assessments/air-treatmentn2/energy-costs-associated-nitrogen-specifications