## Slide 1: Resource Recovery from Human Waste: An overview of nutrient flows and some technologies to recover them
Kindle Williams
Manthiram Lab
Harvard Energy Journal Club
30 April 2021
“One person’s trash is another one’s treasure.”

## Slide 2: Inspiration for this talk: Prof. William Tarpeh, Stanford ChemE/EnvE
tarpehlab.com

## Slide 3: Resource Removal vs. Resource Recovery
Resource Removal:
  Focus on taking something OUT of a waste stream.
  Maybe that thing has a negative impact if not removed.
    e.g.: pathogens
Resource Recovery:
  Focus on MAKING USE of a component in a waste stream
  Allows for waste monetization
  Adds value

## Slide 4: Definitions: Wastewater
What kind of crap will we be talking about today?
Industrial wastewater (pulp & paper, mine drainage, …)
Agricultural runoff
Human excrement (urine + feces)
https://www.aireo2.com/en/markets-2/industrial/pulp-and-paper/
https://flores.unu.edu/en/news/news/safe-use-of-wastewater-in-agriculture-in-practice.html
https://wpde.com/news/local/abc-15-special-report-flushing-away-bad-bathroom-habits
“Sustainable sanitation” / “Ecological sanitation” ideas
Notes: Industrial wastewater
  Pulp and paper:
    S + base to pulp, so this becomes waste as well
    Lots of chlorinated effluent from bleach
    Much organic waste
Ag runoff
  Around 20% of applied N runs off
  Contains N, P, K, pesticides, metals…
“Ecosan” folks focus specifically on reuse to agriculture. This is not necessarily sustainable.

## Slide 5: Composition of human waste
Rose, Parker, Jefferson, Cartmell, Critical Reviews in Environmental Science and Technology 45(17), 1827-1879, 2015.
Solids:
  126 g/person/day
  pH ~6.6
  75% water; solids 84-93% organic
    25-54% bacterial biomass
    2-25% protein/nitrogenous matter
    25% carbohydrate/undigested plant matter
    2-15% fats
    Small amounts of…
      Ca3(PO4)2
      FePO4
      Epithelial cells
      Mucus/intestinal secretions
  Worms & their eggs can also exist in fecal matter. Because of direct handling of untreated waste for ag, Helminthiasis affects ~1.5 BILLION people worldwide.

## Slide 6: Composition of human waste
von Münch, Winker, Technology review of urine diversion components. Deutsche Gesellschaft für Internationale Zusammenarbeit (GIZ) GmBH, 2011.
Liquids (urine):
  1.4 L/person/day
  pH ~6.2
  91-96% water; 59 g solids/person/day
    2% Urea
    0.1% Creatinine
    0.03% Uric acid
    Cl-, Na+, K+, SO42-, NH4+, PO43-
    Small amounts of…
      Organic acids
      Pharmaceuticals
  Makes up 1% of urban wastewater volume but contains 70% of the N
  Urea naturally decomposes to ammonia + CO2
Wikipedia (“Lant”)
https://www.mountainside-medical.com/products/urine-specimen-cup-sterile
Notes: Enzyme urease catalyzes:
Urea + water -> CO2 + 2 Ammonia
Historically, urine used:
As direct fertilizer w/ water dilution
Cleaning agent / teeth whitening
Urine -> straw -> age -> wash -> collect -> dry -> KNO3, a.k.a. saltpeter or gunpowder

## Slide 7: Composition of human waste
Solids
  Contain most of waste C
  Pathogens, trace metals
Liquids
  Contain most of waste P, N, other nutrients
  Not sterile, but minimal pathogens; few trace metals
Despite containing the majority of waste nutrients and posing a lower biological hazard, urine is under-utilized relative to biosolids, especially in developed countries.

## Slide 8: Chemical cycles: Nitrogen
Zeng, Priest, Wang, Wu, Small Methods 4 (12), 2020.
Notes:       Focus on the fact that it’s not a closed loop. We’re losing N to pollution all the time.
      Eutrophication:
      - Increased nutrients (P + nitrate) -> increased biomass -> decreased biodiversity -> hypoxia
      Volatile NOx emissions from FF combustion have led to more N content in precipitation; this has begun to disrupt ecosystems (e.g. southern CA cacti don’t need much N -> invasive species which do need N now entering)

## Slide 9: Chemical cycles: Nitrogen
Figure adapted from Prof. Will Tarpeh’s talk on Tuesday
Numbers: https://slidetodoc.com/ecologywhere-do-i-fit-in-o-study-of/ & Ch. 5 of Environmental Science by Dalhousie Univ.
N2 (~4×109 Gt)
Active Nitrogen (NH4+, NO3-, NO2-, …)
Humans have thrown the N cycle out of balance, leading to pollution
Bio N fixation + lightning
~200 Gt
Denitrification + annamox
~240 Gt
Haber-Bosch
~100 Gt
Waste-water treatment
H-B also contributes ~1.5% of global CO2 emissions.
Recovering all active N from human urine would offset about 1/3 of global ammonia demand.
Notes: We also make a bit of NOx from fossil fuel combustion, which leads to an increase in N content in rain

## Slide 10: Chemical cycles: Phosphorus
Mihelcic, Fry, Shaw, Chemosphere 84(6), 832-839, 2011.
Unlike many resources, P rarely volatilizes
It is, however, a finite resource
  “Peak Phosphorus” debate
Human activity has increased P cycle fluxes 4x
Capture of human excrement could supply ~22% of global P demand
Image: Wikipedia (“Phosphorus Cycle”)
Phosphorus is also a pollutant, but perhaps more urgently, it might be running out.
Notes: Peak P – 2030? Much later?
Morocco/Western Sahara notable for having something like 90% of the world’s phosphate rock

## Slide 11: What happens to human waste today?
Hyun, … , Ray, Annual Reviews of Environment and Resources 44, 287-318, 2019.
2/3 of all human waste is unsafely disposed of
  4+ BILLION people w/o safely managed sanitation
  As of 2015, ~892 Million engage in open defecation (OD)
  Fundamentally a public health problem
Large disparities between high-income countries (HICs) and low- and middle-income countries (LMICs)
  Mid-1800s was time for heavy investment in centralized waste treatment infrastructure
  Large capital investments = large inertia
    Easier (and necessary) to innovate in LMICs
“Sanitation Service Chain”
Notes: Percentages of sewage treated by global region: https://wriorg.s3.amazonaws.com/s3fs-public/uploads/table_1.jpg
90% NA
66% Eur
35% Asia
14% SA/Carib
<1% Afr

## Slide 12: U.S. wastewater treatment: A journey through the sewers
Source: domestic + municipal wastewater, some industrial wastewater (usually pre-treated), sometimes urban runoff/stormwater
Steps:
  Pretreatment: bar screen to remove trash, tree limbs, grit, etc.
    Coagulation & flocculation reagents added
AmritaLearning.com

## Slide 13: U.S. wastewater treatment: A journey through the sewers
Source: domestic + municipal wastewater, some industrial wastewater (usually pre-treated), sometimes urban runoff/stormwater
Steps:
  Pretreatment: bar screen to remove trash, tree limbs, grit, etc.
    Coagulation & flocculation reagents added
  Primary treatment: settling; solid/liquid seps
    Clarifiers skim fat off top, gather sludge on bottom
https://www.tpomag.com/online_exclusives/2017/04/optimize_your_clarifier_for_biological_phosphorus_removal_002y7

## Slide 14: U.S. wastewater treatment: A journey through the sewers
Source: domestic + municipal wastewater, some industrial wastewater (usually pre-treated), sometimes urban runoff/stormwater
Steps:
  Pretreatment: bar screen to remove trash, tree limbs, grit, etc.
    Coagulation & flocculation reagents added
  Primary treatment: settling; solid/liquid seps
    Clarifiers skim fat off top, gather sludge on bottom
  Secondary treatment: remove dissolved/suspended biological matter
    Microbes do the work
Wikipedia (“Constructed Wetland”)
Notes: This is sometimes also done in a clarifier
Fixed-film/attached growth vs. suspended growth

## Slide 15: U.S. wastewater treatment: A journey through the sewers
Source: domestic + municipal wastewater, some industrial wastewater (usually pre-treated), sometimes urban runoff/stormwater
Steps:
  Pretreatment: bar screen to remove trash, tree limbs, grit, etc.
    Coagulation & flocculation reagents added
  Primary treatment: settling; solid/liquid seps
    Clarifiers skim fat off top, gather sludge on bottom
  Secondary treatment: remove dissolved/suspended biological matter
    Microbes do the work
  Tertiary treatment: chemical treatment/filtration
    N removal: Nitrification + Denitrification
    P removal: bioorganisms and/or chemical precipitation
    Disinfection: Ozone, active chlorine, UV light
NH4+
NO3-
N2
Nitrify
De-nitrify

## Slide 16: U.S. wastewater treatment: A journey through the sewers
Source: domestic + municipal wastewater, some industrial wastewater (usually pre-treated), sometimes urban runoff/stormwater
Steps:
  Pretreatment: bar screen to remove trash, tree limbs, grit, etc.
    Coagulation & flocculation reagents added
  Primary treatment: settling; solid/liquid seps
    Clarifiers skim fat off top, gather sludge on bottom
  Secondary treatment: remove dissolved/suspended biological matter
    Microbes do the work
  Tertiary treatment: chemical treatment/filtration
    N removal: Nitrification + Denitrification
    P removal: bioorganisms and/or chemical precipitation
    Disinfection: Ozone, active chlorine, UV light
  4th stage (rare): removal of pharmaceuticals, household chemicals, pesticides, etc.
    Activated carbon filtration
    Enzyme treatment (microbial fuel cells)

## Slide 17: U.S. wastewater treatment: What about folks who are “off-grid”?
Wikipedia (“Septic tank”)
20% of households in the U.S. use a septic tank
Similar principle but just Primary Treatment & distributed
Notes: Common in rural/suburban U.S. and rural Europe

## Slide 18: What we already recover well: solids
Steps in biosolids processing:
  Thicken
  De-water (centrifuge/filter press)
    Liquids sometimes gathered for struvite
  Digest
    Large scale: anaerobic
      Slow but produces methane
    Mid scale: aerobic
      Lower capital cost, higher operating costs; produces CO2
    Small scale: compost
      Mix with other biosolids
Then add to agricultural soil, incinerate, or landfill
Wikipedia (“Sewage sludge treatment”)
Notes: Struvite from de-watering sold in Canada as “Crystal Green” fertilizer

## Slide 19: What we don’t recover well: liquids (N, P)
Nitrification/denitrification is very inefficient
  Traverses thermodynamic landscape
Much waste treatment (e.g. septic) doesn’t even get this far
Dilution (energy intensity) is a major problem
chem.tamu.edu
Nitrification
Denitrification
Haber-Bosch
By the time we’re ready to re-apply N to soil, we’ve returned to where we started!

## Slide 20: Source-separation & dry urine collection allows us to directly process urine
http://www.bbs.bt/news/?p=93609
Other types of waste treatment more commonly used in LMICs…
Pour-flush toilets
Dry toilets: Urine-diverting
Dry toilets: Composting
Dry toilets: Pit latrine
Wikipedia (“Pit latrine”)
Wikipedia (“Composting toilet”)
By SuSanA Secretariat - Cleaning a urine-diverting dry toilet (UDDT) in Johannesburg Uploaded by Elitre, CC BY 2.0, https://commons.wikimedia.org/w/index.php?curid=22164302
Notes: High-temperature treatment required to remove pathogens from solids (e.g. Helminth eggs)

## Slide 21: Technologies for N recovery from urine: adsorption
Seeker: “How your pee could help billions of people.” https://www.youtube.com/watch?v=eQV2bOYXbKc
An established method for separation of ionic species
Adsorb NH3 to acid sites of ion exchange resin
Recover with acid flush
In some cases, can apply the adsorbent directly to agricultural soil
Notes: Natural zeolites w/ adsorbed N can be applied to soil

## Slide 22: Technologies for N recovery from urine: electrochemical stripping
Adapted & taken from Tarpeh et al., Environ. Sci. Technol. 52, 1453-1460, 2018.
Beginning to overtake static-adsorptive processes in promise
Benefits from conductivity of source-separated urine
Play with pH
Urine
Anode chamber (low pH)
Cathode chamber (high pH)
Trap chamber
(low pH)
OER:
V
HER:
Cation exchange membrane
Gas permeable membrane
NH4+ (aq)
OH- (aq) + NH4+ (aq) NH3(aq) + H2O
NH3(g)
NH3(aq) + H+(aq) NH4+(aq)
Notes: Removal and recovery efficiencies for this process can be upwards of 90%

## Slide 23: Technologies for N/P recovery from urine: others
Kogler, … , Tarpeh, ACS EST Engg. 1(4), 662-684, 2021.
Combined adsorption + EChem regeneration
Biological vs. Physicochemical

## Slide 24: Zooming back out: the engineering/environmental perspective of sanitation
Resource efficiency & pollution just some of many things to think about within sanitation
Hyun, … , Ray, Annual Reviews of Environment and Resources 44, 287-318, 2019.

## Slide 25: The place of waste treatment innovation in the global economy
High-income nations = slow to change (large investments)
Low/middle-income nations = rapidly improving sanitation, can quickly adopt tech
What works in one place doesn’t necessarily work in all
Hyun, … , Ray, Annual Reviews of Environment and Resources 44, 287-318, 2019.

## Slide 26: What should we chat about?
Contact me:
Kindle Williams
kindlew@mit.edu
Thanks for listening!

## Slide 27: Composition of human waste
von Münch, Winker, Technology review of urine diversion components. Deutsche Gesellschaft für Internationale Zusammenarbeit (GIZ) GmBH, 2011.
Liquids (urine):

## Slide 28: References
Broader societal picture of sanitation: C. Hyun, Z. Burt, Y. Crider, K. L. Nelson, C. S. S. Prasad, S. D. G. Rayasam, W. A. Tarpeh, and I. Ray. “Sanitation for Low-Income Regions: A Cross-Disciplinary Review,” Annual Review of Environment and Resources (2019). https://doi.org/10.1146/annurev-environ-101718-033327
Tech review: A. Kogler, M. Farmer, J. Simon, S. Tilmans, G. Wells, W. A. Tarpeh. “A systematic evaluation of emerging wastewater nutrient removal and recovery technologies to inform practice and advance resource efficiency,” ACS ES&T Engineering (Accepted Feb 2021). https://doi.org/10.1021/acsestengg.0c00253
Deeper into techs: W. A. Tarpeh, X. Chen. “Making wastewater obsolete: Selective separations to enable circular water treatment,” Environmental Science and Ecotechnology (2021). https://doi.org/10.1016/j.ese.2021.100078
Electrochemical stripping: W. A. Tarpeh, J. M. Barazesh, T. Y. Cath, K. L. Nelson. “Electrochemical Stripping to Recover Nitrogen from Source-Separated Urine,” Environmental Science & Technology (2018). https://doi.org/10.1021/acs.est.7b05488
Adsorption: W. A. Tarpeh, K. M. Udert, K. L. Nelson. “Comparing ion exchange adsorbents for nitrogen recovery from source-separated urine,” Environmental Science & Technology (2017). https://doi.org/10.1021/acs.est.6b05816
For an overview of the Tarpeh Lab’s publications, please see: https://www.tarpehlab.com/publications

## Slide 29: Ammonia uses by humans
Scheme: Nik Lazouski

## Slide 30: Fertilizers support the global population

## Slide 31: The current process: Haber-Bosch
Ahmad, S. ud D. 2015
1.9-9 ton CO2/ton NH3
>450 million tons CO2/yr
Only economically viable at large scales
  ~3000 ton/day
Centralized production
Large capital cost
  $1B+ per plant
Out of reach for many less-wealthy economies

## Slide 32: Two components: H2 production and ammonia synthesis
1: Hydrogen Production
2: Ammonia Synthesis
“Colors” of H2:
  Grey
  Blue
  Green
  Turquoise
Haber-Bosch
Plasma-based approaches
Electrochemical approaches
scale match
Notes: Note: almost half of industrially produced H2 goes to ammonia synthesis.

## Slide 33: Ammonia synthesis: thermodynamics & kinetics
Thermochemical
Conversion
X
Higher pressures to achieve reasonable conversions
X <20%
Higher temperatures to achieve reasonable rates
1/2 N2 + 3/2 H2  NH3
Electrochemical
At ambient pressure (1 atm):
X
Voltage also improves kinetics, so can operate at lower temperature
Apply voltage to increase conversion
X > 99%
Z. J. Schiffer and K. Manthiram Joule 1 10-14 (2017).
Hard to break the N2 triple bond

## Slide 34: How does this fit into the big picture of sustainability?
Nitrogen cycle
  Inherent N losses to soil during fertilization
  N oxides are also greenhouse gases
Distributed fert. production could help with slower fert. application
  Less runoff