## Slide 1
Nuclear fission reactors and their fuel cycles
HEJC
Feb 26, 2020
Eric Fell

## Slide 2: Nuclear Power in the U.S.
94 nuclear reactors currently operating in USA (~97 GW)
19% of the nation’s total electric energy generation
Accounts for ~60% of U.S. emission-free energy generation
(2021) US Energy Information Administration
https://www.eia.gov/totalenergy/data/monthly/pdf/mer.pdf
Globally, ~442 nuclear power plants totaling 392 GWe

## Slide 3: Fundamentals of Nuclear Reactions
http://fys246.nuclear.lu.se/topics.asp
All elements have isotopes, large range of stabilities
Radioactive decay occurs in unstable isotopes, resulting in spontaneous emission of particles and/or electromagnetic radiation
To provide sufficient attractive force for stability, number of neutrons (N) increases more rapidly than number of protons (Z), with N/Z ratio: 1 (light nuclei) increasing to ~1.5 (at bismuth)

## Slide 4: Barriers in Nuclear Reactions
Charged particles must overcome electrostatic potential energy barrier for nuclear reactions to occur
  Barrier scales with Z, on the order of a few MeV per proton pair
  abundance of charged reactants (e.g. protons in elements)
  Can overcome barrier with kinetic energy, propelled by electromagnetic fields of an accelerator etc.
Neutral particles have no electrostatic potential barrier
  Neutrons require less kinetic energy to initiate nuclear reactions
  Free neutron is short lived (lifetime ~15 min), therefore source is required for any use of neutrons

## Slide 5: Binding Energy
Nuclear transmutations release energy equal to the difference between binding energy of nuclei in final and initial states

## Slide 6: Mass-Energy Equivalence
Energy of nuclear decay comes from mass conversion, on the energy scale of MeV (1.6⨯10-13 J) released for every nuclear reaction

## Slide 7: Fission Reactor
Thermal neutrons are captured by fissile fuel
Fuel fissions, releasing fast neutrons and energy
Fast neutrons are slowed by the moderator

## Slide 8: Important Reactor Parameters
Neutron energy
Thermal: (RT=0.025 eV) typical speed after being moderated
Fast: >1 MeV, typical speed when emitted from fission reaction
Neutron cross section
Likelihood of interaction between neutron and target nucleus
Cross sections for capture, for scattering, for fission etc.
Highly dependent on neutron energy
Neutron flux
Amount of neutrons produced per area per time
Fission reactor < fusion reactor ≤ accelerator driven system
Subcritical: k<1 Critical: k=1 Supercritical: k>1
Neutron multiplication factor k
Notes: Tradeoffs abound: high flux, easier to burn up waste products, easier for 2 neutron capture etc.; low flux, sometimes easier for desired fission to occur

## Slide 9: Fission Reactor Fuels
Fertile
(can be converted to fissile fuel)
Fissile
(can sustain fission chain reaction)
Fissionable
(can fission)
241Pu
233U
235U
239Pu
238U
232Th
234U
Many actinide isotopes
Notes: Just showing naturally occurring fertile material

## Slide 10: Fission Reactor Fuels: Uranium-235
  • Naturally occurring but in low abundance (uranium is found >99% as U-238)
  • Can be used in heavy water reactors (unenriched uranium) or light water reactors (enriched uranium)
  • Requires thermal (slow) neutrons for adequate fission, so a moderator is required
  • World’s primary nuclear fissile fuel
 | % U-235
Naturally occurring | 0.7
Reactor grade | 3-5
Weapons grade | 20-85
https://en.wikipedia.org/wiki/Decay_chain
235U Natural decay chain
t1/2 = 7x108 y

## Slide 11: Fission Reactor Fuels: Plutonium-239
  • Bred from 238U
  • Smaller critical mass, cheaper than enriched 235U so it’s often used in nuclear weapons
Breeding is typically done in a Fast Reactor because fast neutrons are more efficient at plutonium production
Breeding process can create 240Pu which is an undesirable contaminant, and a dangerous gamma-emitter
 | % Pu-240
Supergrade (Navy nukes) | 2-3
Weapons grade | 3-7
Fuel grade | 7-18
Reactor grade | >18
239Pu will accumulate over time in normal fission reactor using uranium, with spent fuel being ~0.8% 239Pu
fast
t1/2 = 2.4x104 y

## Slide 12: Fission Reactor Fuels: Uranium-233
Fissions with thermal neutrons
Neutrons & Energy
Neutrons contribute to breeding
Require small amount of initial fissile fuel
  • Bred from 232Th which is ~3-4 times more abundant than uranium on Earth
  • Can be bred using fast neutrons or thermal neutrons
t1/2 = 1.6x105 y

## Slide 13: Neutron Cross-Section for Fission
https://www.world-nuclear.org/information-library/nuclear-fuel-cycle/introduction/physics-of-nuclear-energy.aspx
~Probability that fission will occur
Neutrons need to be slowed (moderated) to induce significant fission

## Slide 14: Fission Reactor Classes
Light water reactors
  Pressurized water (PWR)
  Boiling water (BWR)
  RBMK (LWGR)
Heavy Water reactors
  Pressurized heavy water (PHWR or CANDU)
Gas cooled reactors (GCR)
Fast Neutron reactors (FNR)
More than two thirds of the reactors in the world are PWR designs
https://www.world-nuclear.org/our-association/publications/global-trends-reports/world-nuclear-performance-report.aspx

## Slide 15: Pressurized Water Reactor
https://en.wikipedia.org/wiki/Light-water_reactor
Water is used as both a neutron moderator and a coolant
Primary and secondary coolants are isolated from each other, containing the radioactivity within the primary loop
Water never boils in the reactor, as primary loop is maintained at ~155 Bar
Using water provides the PWR with stability: negative temperature coefficient
If reactivity gets too high, water will expand and be a less effective moderator
 Neutrons aren’t slowed as much, reactivity goes down

## Slide 16: Boiling Water Reactor
https://en.wikipedia.org/wiki/Light-water_reactor
Similar to PWR but water is turned to steam in the reactor, and one continuous coolant/moderator loop is used instead
High purity water must be used
Trace radioactivity due to neutron capture from water means a larger maintenance cost for turbine protection but this is usually offset by cost savings of a simpler design and thermal efficiency compared to PWR

## Slide 17: PWR/BWR Fuel Cycle
Typically utilize low-enriched uranium as fuel
80-100 tonnes used in a PWR, 100-140 in a BWR
Refuel on 18-24 month cycle, usually one third of fuel is replaced during refueling
http://nuclearsafety.gc.ca/eng/reactors/power-plants/nuclear-power-plant-safety-systems/index.cfm

## Slide 18: Mixed Oxide (MOX) Fuel
https://www.world-nuclear.org/information-library/nuclear-fuel-cycle/fuel-recycling/mixed-oxide-fuel-mox.aspx
Pu can be recovered from used reactor fuel and mixed with depleted U, forming MOX
MOX fuel provides ~5% of new fuel used today (>10% in France)
Weapons-grade Pu can also be burned up through MOX fuel
Each year about 70 tonnes of plutonium (contained in used fuel) is removed from the world’s reactors

## Slide 19: RBMK (Light Water Graphite Reactor)
https://www.world-nuclear.org/information-library/nuclear-fuel-cycle/nuclear-power-reactors/appendices/rbmk-reactors.aspx
Each fuel assembly in its own pressure tube, cooled by pressurized water
Pressure tubes surrounded by graphite blocks which act as moderator
Graphite moderator allows for use of unenriched U. This let the USSR build very large, very cheap reactors
Major difference compared to other LWRs: positive temperature coefficient
If reactivity gets too high, water will expand and be a less effective coolant/moderator, but the graphite continues to moderate
Extra free neutrons increases reactivity
(this was a significant contributor to the Chernobyl accident)

## Slide 20: CANDU (Canadian Deuterium) Reactors
https://en.wikipedia.org/wiki/CANDU_reactor
By using heavy water (D2O) which has a much lower neutron cross section than water, natural uranium can be used
Cost of enrichment is removed, an advantage in nuclear proliferation terms
Calandria is not pressurized in CANDU reactor, only individual fuel rod pressure tubes
System can be refueled online, and reactor vessel is easier to make

## Slide 21: Gas-Cooled Reactors
Graphite moderator with CO2 used as coolant, burns low-enriched uranium
Coolant leaving the reactor is maintained at higher temperature than PWR/LWR, allowing for higher thermal efficiency
Can be refueled online
Due to reactor design, fuel burnup is not as efficient and so the reactor has to be larger for same power output
https://en.wikipedia.org/wiki/Advanced_Gas-cooled_Reactor

## Slide 22: Fast Neutron Reactors
235U and 239Pu are less fissionable with high energy neutrons but enrichment can make the fuel usable
Removal of moderator reduces reactor size, complexity
Breeder reactors can use a moderator surrounding by blanket of depleted uranium to breed more 239Pu than it consumes
Coolants are typically liquid metals (Na, Pb-Bi) or helium gas
Can use nuclear waste as fuel
Have so far proved costly due to enrichment requirements and current low prices for uranium
https://www.world-nuclear.org/information-library/current-and-future-generation/fast-neutron-reactors.aspx

## Slide 23: Fission Waste
Distribution of fission products
Activity of high-level waste from one tonne of used fuel
https://www.world-nuclear.org/information-library/nuclear-fuel-cycle/introduction/physics-of-nuclear-energy.aspx
Possible fissions

## Slide 24: References
Choppin, Liljenzin, Rydberg, Ekberg, Radiochemistry and Nuclear Chemistry
Chart of Nuclides
World Nuclear Association
IEA nuclear
EIA nuclear