## Slide 1
Nuclear Batteries
HEJC
Sep 25, 2020
Eric Fell

## Slide 2: Fundamentals of Nuclear Reactions
http://fys246.nuclear.lu.se/topics.asp
All elements have isotopes, large range of stabilities
Radioactive decay occurs in unstable isotopes, resulting in spontaneous emission of particles and/or electromagnetic radiation
Repulsive force between protons must be balanced by a strong attractive force for nuclei stability

## Slide 3: Types of Nuclear Decay
Other decay processes include
Gamma decay
Neutron emission
Electron capture
Internal conversion
Cluster decay / fission

## Slide 4: Mass-Energy Equivalence
Energy of nuclear decay comes from mass conversion, on the energy scale of MeV (1.6⨯10-13 J) released for every nuclear reaction

## Slide 5: Binding Energy
Nuclear transmutations release energy equal to the difference between binding energy of nuclei in final and initial states

## Slide 6: Battery/Energy Storage Device
 |  | Rechargeable? | 
 |  | Yes | No
Electrochemical? | Yes |  | 
 | No |  | 

## Slide 7: Nuclear Batteries
Generate electricity from nuclear decay, without chain reactions
Thermal Conversion
Thermoelectric
  Radioisotope thermoelectric generators (RTG)
Thermionic
  Radioactive ‘hot’ electrode emits electrons over space-carrier barrier to a cooler electrode
Non-Thermal Conversion
Electrostatic
  Charged particle buildup on a conductor
Radiovoltaic
  Alpha/beta/gamma/neutron ionizing radiation through semiconductors
Optoelectric
  Radioluminescent material used, light converted to electricity

## Slide 8: Radioisotope Thermoelectric Generators (RTGs)
Convert heat from radioisotope decay into electricity, using thermocouples.
Isotope | Primary decay | Shielding required | Power density (W/g) | Half-life (years)
238Pu | α | Low | 0.54 | 88
90Sr | β- | High | 0.46 | 29
210Po | α | Low | 140 | 0.4
241Am | α | Medium | 0.11 | 432
https://en.wikipedia.org/wiki/Radioisotope_thermoelectric_generator
238PuO2 pellet, initially 62 W
SiGe semiconductor thermocouples typically used due to their low sensitivity to radiation damage
Overall efficiency typically <10%
1 g of 238Pu generates 0.6 W

## Slide 9: Radioisotope Thermoelectric Generators (RTGs) cont.
Electric potential build up across a temperature gradient
Seebeck effect
RTGs use many thermocouples in series to get a usable voltage
238PuO2
Atmosphere/coolant

## Slide 10: Radioisotope Thermoelectric Generators (RTGs) cont.
Curiosity rover uses an RTG with 11 lbs of 238PuO2
Voyager 1,2 use 3 RTGs @157 W each

## Slide 11: Pacemakers
1967, Atomic Energy Commission
Also an RTG design using 238PuO2
Quickly replaced by lithium batteries once they became available
Some designs used 147Pm in Betavoltaic device

## Slide 12: Betavoltaics
Generate electric current from beta particle emission, using semiconductor junctions.
Tritium is often used as it produces less radiation, half-life ~12.3 years
Beta emission generates electron-hole pairs which separate due to built-in electric field. Accumulation of separated charge across np-junction leads to current flow through external circuit
Similar to photovoltaics, except much smaller currents

## Slide 13: Betavoltaics cont.
Isotope | Average β Energy (keV) | Maximum β Energy (keV) | Half-life (years)
3H | 5.7 | 18 | 12.3
63Ni | 18 | 67 | 92
147Pm | 62 | 225 | 2.6
Because radiation damage of the semiconductor is a concern, β energy typically needs to be <300 keV
Betavoltaics have niche low-power applications:
Medical implants (pacemakers, pre ~1980s)
Outer space
IOT devices, electronics
Trickle-charging
‘High’ efficiency betavoltaic is typically 6-8%
Commercialized ‘Betacel’ 1970s

## Slide 14: Who’s currently working on Betavoltaics?
Spinout from Cornell, founded 2008
Still early stage commercialization, with VC funding from Lockheed and support from DOD
Tech is silicon carbide betavoltaic, tritium or nickel, 2-6 V @ 1μW max
Miami-based, founded 2005
All betavoltaic products use tritium
1-2.4 V @ 100μW max

## Slide 15: Betavoltaic “Diamond Battery”
Younger startup out of the Bay Area
Advertise devices that are diamond-based, alpha/beta/neutron voltaic batteries
No actual product reported yet
Instead of using silicon as a semiconductor, replace it with doped diamond (5.5eV bandgap) which has a much higher resistance to radiation damage.
https://www.sciencedirect.com/science/article/pii/S0925963517307495?via%3Dihub
Using low-enriched 63Ni, 10μW/cm3 can be achieved

## Slide 16: Betavoltaic “Diamond Battery” part 2
Idea is to turn radioactive graphite (waste from decommissioned fission reactors, UK has a bunch), into diamond for battery active material
Remove 14C from graphite and synthesize artificial diamond structure
 Half-life is 5730 years so this would not be a high power density device

## Slide 17: Future of Nuclear Batteries?
RTG onboard Mars rover Perseverance, currently en route to Mars
RTG tech is very much developed, next-gen continually being researched by academia, industry etc.
Developed Betavoltaic tech does have a significant avenue in the low-power device market. Will likely continue to grow as interest in IOT, MEMS, trickle-charging develops
Ignore the hype: we won’t see nuclear batteries in cars. Ever. And we don’t need millennia-lasting devices

## Slide 18: Further Reading
Choppin, Liljenzin, Rydberg, Ekberg, Radiochemistry and Nuclear Chemistry
Chart of Nuclides
City labs
Widetronix
NDB inc.