## Slide 1: How enhanced oil recovery may perpetuate the climate crisis instead of helping address it
Toly Rinberg
HEJC 10/9/20

## Slide 2
Fossil resources
11,000 GtCO2
Global cumulative emission bound to stay below 2C warming:
(2011-2050)
~1000 GtCO2
McGlade & Ekins (2015)
Reserves
3000 GtCO2

## Slide 3: Focus on emissions and oil in the U.S.
In 2019, U.S. petroleum emissions = 2.4 GtCO2 / year
Current U.S. emissions = 6.7 GtCO2 / year
Cumulative U.S. emissions = 400 GtCO2
https://www.eia.gov/energyexplained/oil-and-petroleum-products/use-of-oil.php
Notes: which included about 1.1 million b/d of biofuels.
7.5 billion barrels of oil consumed in 2018 - https://www.eia.gov/tools/faqs/faq.php?id=33&t=6

## Slide 4: Original oil in place, production, and reserves
(2008)
Some rough CO2 accounting:
Original oil in place: 300 GtCO2
Cumul. Production: 86 GtCO2
Reserves: 11 GtCO2
Remaining: 200 GtCO2
Recall: Cumul. U.S. emissions = 400 GtCO2
Note: 1 barrel of oil ~= 0.5 lifecycle tCO2 emissions
https://www.netl.doe.gov/sites/default/files/netl-file/CO2_EOR_Primer.pdf

## Slide 5
Where is this going!?
What the frack
“I am not banning fracking”

## Slide 6: Fossil fuels unlocked through EOR?
(2008)
~85 billion barrels of oil are technically recoverable through CO2-EOR
(=43 GtCO2)
*Note: this doesn’t count next gen EOR that adds +40 billion barrels
https://www.netl.doe.gov/sites/default/files/netl-file/CO2_EOR_Primer.pdf
Proved Reserves
43.8 billion barrels (2018)

## Slide 7: Oil production in the U.S. today
Total oil produced:
~4.5 billion barrels / year
Oil from EOR (~2%):
~100 million barrels/year
https://www.eia.gov/dnav/pet/PET_CRD_CRPDN_ADC_MBBLPD_A.htm
https://www.eia.gov/energyexplained/oil-and-petroleum-products/where-our-oil-comes-from.php

## Slide 8: U.S. emissions from consumed oil
2020
2050
2.3
GtCO2
0
34.5 GtCO2
=
~70 billion barrels of oil
Compare to:
Proven U.S. reserves = 44 billion barrels of oil (22 GtCO2)
Oil unlocked with EOR = 85 billion barrels of oil (43 GtCO2)
https://www.eia.gov/outlooks/steo/report/renew_co2.php?src=Environment-b1
Notes: 7.5 billion barrels of oil consumed in 2018 - https://www.eia.gov/tools/faqs/faq.php?id=33&t=6
Which number is right?
https://en.wikipedia.org/wiki/Oil_reserves_in_the_United_States
https://www.statista.com/statistics/236687/proven-crude-oil-reserves-in-the-usa-since-1980/

## Slide 9
http://large.stanford.edu/courses/2013/ph240/salehi2/docs/netl-2010-1417.pdf

## Slide 10: Oil production and EOR

## Slide 11: The phases of oil well production
Primary recovery - Pop open the well and let internal pressure and processes drive extraction.
Secondary recovery – External energy applied to increase well pressure, typically by injecting water or gas
Tertiary (or enhanced) recovery - Increase the mobility of the oil in order to increase extraction (CO2-EOR 60%, Thermal-EOR 40%, Chemical-EOR 1%)

## Slide 12
https://www.frontiersin.org/articles/10.3389/fclim.2019.00005/full

## Slide 13: Case study: Shell Oil’s Denver Unit in the Wasson Field in West Texas
https://www.netl.doe.gov/sites/default/files/netl-file/CO2_EOR_Primer.pdf
Initial oil in place: 2 billion barrels
Field started producing oil in 1938!

## Slide 14
https://www.globalenergyinstitute.org/sites/default/files/020174_EI21_EnhancedOilRecovery_final.pdf

## Slide 15: Current EOR infrastructure
https://www.netl.doe.gov/sites/default/files/netl-file/CO2_EOR_Primer.pdf
CO2 Domes in Colorado:
Notes: +4000 miles of pipeline

## Slide 16: How to think about sequestration and EOR?

## Slide 17: What happens with the CO2 that is injected during EOR?
Most of CO2 injected during EOR ends up getting trapped in the subsurface
Amount of CO2 needed per barrel of oil over time is highly variable [see back up slide]
Historical average is ~0.5 tCO2 stored / barrel of oil produced
  Careful: ***Big caveat on this number***
  Recall: 1 barrel of oil combusted = 0.5 lifecycle tCO2 emissions
  Note: don’t forget about legacy emissions from oil recovered from the well
But to evaluate the significance of these numbers, we have to ask where the CO2 comes from…

## Slide 18: Underground CO2 (re)sequestered
https://www.iea.org/commentaries/can-co2-eor-really-provide-carbon-negative-oil
*Almost all EOR is done this way today
Today, comes from: underground domes, mostly in Colorado

## Slide 19: Anthropogenic CO2 sequestered
https://www.iea.org/commentaries/can-co2-eor-really-provide-carbon-negative-oil
Small % of EOR done this way
Today, comes from: Ammonia, ethanol production, natural gas
Fossil fuel

## Slide 20: Atmospheric CO2 sequestered
https://www.iea.org/commentaries/can-co2-eor-really-provide-carbon-negative-oil
No EOR done this way (some projects under development)

## Slide 21: Back of the envelope on: Sequestration and EOR costs
Cost of:
  Sequestration: $10-20 / tCO2
  EOR: $15-25 / barrel oil out: ~$30-50 / tCO2
+ cost of CO2
  Underground CO2 : ~15 t/CO2
  CCS: +$40 t/CO2
  DAC: +$500 t/CO2
https://www.netl.doe.gov/sites/default/files/netl-file/CO2_EOR_Primer.pdf
Notes: NAS 2019 Negative Emissions Report
EOR project example: http://large.stanford.edu/courses/2013/ph240/salehi2/docs/netl-2010-1417.pdf
https://web.archive.org/web/20191231185457/http://cornerstonemag.net/understanding-the-national-enhanced-oil-recovery-initiative/

## Slide 22: What would it take to even out the costs?
Rough balance:
  Sequestration: $10-20 / tCO2
  EOR: $30-50 / tCO2
45Q Tax Credits
  $50/ton for anthropogenic CO2 sequestered outside of EOR
  $35/ton for anthropogenic CO2 sequestered by EOR
+ cost of CO2
  - tax/subsidy
  - oil sale - tax/subsidy
Note: no modest tax/subsidy could close the DAC gap given current CO2 DAC costs of +$500 t/CO2
https://www.netl.doe.gov/sites/default/files/netl-file/CO2_EOR_Primer.pdf
Notes: NAS 2019 Negative Emissions Report
EOR project example: http://large.stanford.edu/courses/2013/ph240/salehi2/docs/netl-2010-1417.pdf
https://web.archive.org/web/20191231185457/http://cornerstonemag.net/understanding-the-national-enhanced-oil-recovery-initiative/

## Slide 23: The EOR operator’s choice determines everything about carbon balance
Underground CO2 [~$15/tCO2]
Anthropogenic (CCS) [+$40/tCO2]
Direct air capture [+$500/tCO2]
CO2-EOR Rig
https://www.nap.edu/catalog/25259/negative-emissions-technologies-and-reliable-sequestration-a-research-agenda
Notes: NAS 2019 Negative Emissions Report - https://www.nap.edu/catalog/25259/negative-emissions-technologies-and-reliable-sequestration-a-research-agenda

## Slide 24: Three main arguments being put forward supporting EOR
EOR enables CO2 sequestration
EOR enables “learning by doing” for CCS and Direct Air Capture, even without a sequestration benefit (or with net emissions)
Isn’t “lower carbon” oil better?

## Slide 25: How much does EOR enable CO2 sequestration
“Employing “next generation” CO2-EOR technology would create CO2 storage capacity in domestic oil fields of over 28 gigatons, equal to captured CO2 emissions from 151 GWs of coal-fired power plants (for 30 years)”
http://large.stanford.edu/courses/2013/ph240/salehi2/docs/netl-2010-1417.pdf

## Slide 26: Storage capacity with and without EOR
Without EOR
  DOE's Carbon Utilization and Storage Atlas Estimates at Least 2,400 Billion Metric Tons of U.S. CO2 Storage Resource
With EOR
  👏this👏 is👏 irrelevant 👏 the current capacity is already so massive
  Note: Cumulate global emissions = 1,500 GtCO2
https://www.energy.gov/fe/articles/does-carbon-utilization-and-storage-atlas-estimates-least-2400

## Slide 27: CO2-EOR and “learning by doing”

## Slide 28: EOR is the largest industrial use of CO2 Total market size: ~100 MtCO2

## Slide 31
This study does not evaluate the scenario where CO2 sequestration is treated as waste management (also no discussion of technological lock-in)
What if you pay people to just put (CCS or DAC) CO2 in the ground?
Notes: On average, ~$150/ton is spent on managing waste, which is globally produced at approximately ~2Gt/year (growing to 3.4 by 2050). Still need to figure out financing and revenue models.
$205 billion (2012) to $375 billion (2025)

## Slide 32: Isn’t “lower carbon” oil better?

## Slide 33: Why shouldn’t we care about “lower carbon” oil?
The climate target is: atmospheric CO2
The decision to decarbonize society is a political one
If we need a certain amount of oil – great, let’s produce that oil
  Current policy instruments are designed not to change the price of oil
  So, we can just ask how much oil can be consumed (given the particular emissions reduction rate we enforce and rate of societal change we permit)
If we need to sequester a certain amount of CO2 – great, let’s sequester that much
  We could set up a waste management system for the CO2 to be removed

## Slide 34: Current EOR market policies and their failures

## Slide 35: Current U.S. market-based policy landscape
45Q Tax Credits
  $35/ton for CO2 sequestered by EOR
  $35/ton for other beneficial uses of CO2 (e.g., synthetic fuels or plastics — my next article will be on this)
  $50/ton for CO2 sequestered outside of EOR.
California’s Low Carbon Fuel Standard
  Credit traded at an average around $175/tCO2

## Slide 36: Issues with regulating market-policy: A tax fraud case study
U.S. Treasury Inspector General for Tax Administration (TIGTA) revealed in April 2020: fossil fuel companies improperly claimed nearly $1 billion in clean air 45Q tax credits
  Reason: noncompliance with EPA’s monitoring, reporting, and verification (MRV) requirements
“Of the ten companies claiming 99.9 percent of the 45Q credits, TIGTA found that only three had the required plans in place with the EPA … hundreds of millions of improperly claimed taxpayer dollars remain unchallenged by the IRS.”
https://www.menendez.senate.gov/imo/media/doc/TIGTA%20IRC%2045Q%20Response%20Letter%20FINAL%2004-15-2020.pdf

## Slide 37: What worlds lie ahead?
Market world
Pedal on the break, pedal on the gas:
  CO2 is a large cost, so operators will minimize its use as much as possible
  EOR unlocks >85 billion barrels of oil (>43 GtCO2 emissions) and creates big incentive for profit
  Fraud is already evident
“Learning by doing” for DAC isn’t feasible; for CCS must be evaluated with CO2 waste management counterfactual
Currently almost all CO2 for EOR comes from domes, NOT anthropogenic/atmospheric sources
EOR operator decisions extremely sensitive to price of oil
Technological lock-in not accounted for
Reasonable world
Decouple sequestration targets from oil production targets
Does not muddy incentive for oil and drive for sequestration
Allows for targeting DAC if necessary, rather than setting up competition between CCS and traditional oil production
Avoids technological lock-in problem