## Slide 1: A Presentation of Ice & Fire: Thermal Energy Storage
Dr. Mandy Liu
2023/04/28
Bye bye HEJC and Eric

## Slide 2: Definition & History of Thermal Energy Storage
“TES is the temporary storage of energy by heating or cooling a storage medium so that the stored energy can be used at a later time (for power generation/heating & cooling).”
European Association for Storage of Energy, 2017
Paksoy, Thermal Energy Storage for Sustainable Energy Consumption, 3–22.
IRENA, Innovation Outlook: Thermal Energy Storage, 2020
storing food over ice
conditioning the room with ice & convection

## Slide 3: Case Studies: TES with Natural Resources
Downtown Toronto has the largest deep lake water cooling (DLWC) system in the world.
How well it works:
Saves 90 K MWh of electricity annually
  (70% of cooling demand)
Saves 220 million gallon of water
Potential pitfall:
Sensitive to global warming
Warm discharge water could lead to algae bloom
Washington Post
Notes: https://www.washingtonpost.com/climate-solutions/interactive/2021/toronto-deep-latke-water-cooling-raptors/
https://www.google.com/search?q=Sundsvall+hospital+cooling+plant&rlz=1C1CHBF_enUS890US890&source=lnms&tbm=isch&sa=X&ved=2ahUKEwj1vZze7sj-AhU9EVkFHcgIDf4Q_AUoAnoECAEQBA&biw=1671&bih=884&dpr=1.35#imgrc=-7hYl9hCLLxW0M

## Slide 4: Case Studies: TES with Natural Resources
Successful snow cooling system in Sundsvall Hospital, Sweden.
How well it works:
Saves 90% of electricity needed for cooling
  900 MWh -> 65 MWh (heat pumps)
Saves cost to deposit snow
Potential pitfall:
Sensitive to global warming
Works the best for places with long winter and peak summer cooling demand
Interreg Europe
Notes: https://www.washingtonpost.com/climate-solutions/interactive/2021/toronto-deep-latke-water-cooling-raptors/
https://www.google.com/search?q=Sundsvall+hospital+cooling+plant&rlz=1C1CHBF_enUS890US890&source=lnms&tbm=isch&sa=X&ved=2ahUKEwj1vZze7sj-AhU9EVkFHcgIDf4Q_AUoAnoECAEQBA&biw=1671&bih=884&dpr=1.35#imgrc=-7hYl9hCLLxW0M

## Slide 5: TES towards clean energy transition
Key benefits: Enabler for renewable energy adaptation
Current status, market size & growth
Technology overview
  4 mechanisms
Application by Sector
  Power, heating & cooling (district & individual buildings), transport (cold chain), industry (high-temperature)
Barriers to overcome & potential solutions
IRENA, Innovation Outlook: Thermal Energy Storage, 2020
Notes: Investment comparison: https://www.irena.org/News/pressreleases/2023/Feb/Investments-in-Renewables-Reached-Record-High-But-Need-Massive-Increase-More-Equitable-Distribution#:~:text=Despite%20reaching%20record%2Dhigh%20annual,grids)%20between%202021%20and%202030.

## Slide 6: Key Benefits of TES: enabling clean energy transition
Bridge the intermittency of solar & wind, at much lower unit cost compared to Li-ion battery (some could be 60–90% cheaper).
Notes: Investment comparison: https://www.irena.org/News/pressreleases/2023/Feb/Investments-in-Renewables-Reached-Record-High-But-Need-Massive-Increase-More-Equitable-Distribution#:~:text=Despite%20reaching%20record%2Dhigh%20annual,grids)%20between%202021%20and%202030.

## Slide 7: Key Benefits of TES: enabling clean energy transition
With high flexibility, TES can be the “glue” of a clean-energy society.
Notes: Investment comparison: https://www.irena.org/News/pressreleases/2023/Feb/Investments-in-Renewables-Reached-Record-High-But-Need-Massive-Increase-More-Equitable-Distribution#:~:text=Despite%20reaching%20record%2Dhigh%20annual,grids)%20between%202021%20and%202030.

## Slide 8: Current status & market overview
Expected to triple by 2030 (> 800 GWh)
Expected investment: $ 13-27 billion
  Global investment in renewables in 2010-2019: $ 2.5 trillion
UN Environment Programme
  ATES (aquifer): some of the largest heating and cooling projects

## Slide 9: Technology Overview
4 main mechanisms: sensible, latent, thermochemical, mechanical-thermal heat storage
Energies
Sensible vs latent heat storage
Sensible heat: changing the temperature of a medium
  (water) tank TS
  solid-state TS (bricks, rocks, concretes)
Latent heat: heat change related to a phase change
  ice TS
  phase-change materials (PCM)

## Slide 10: Technology Overview
4 main mechanisms: sensible, latent, thermochemical, mechanical-thermal heat storage
Thermochemical storage involves triggering chemical reactions (typically decomposition & formation), or sorption & desorption
Mechanical-thermal storage involves compressing air:
compressed air energy storage (CAES): off peak electricity used to compress air. Peak: expended air drives turbine.
Liquid air ES: air is compressed so much that it liquifies

## Slide 11: Technology Overview

## Slide 12: Application by sectors: Power
The journal of energy storage
most common example: molten-salt @ concentrating solar plants, will be paired with 70% of CSP. Main challenge: salt freezing.

## Slide 13: Application by sectors: Industry
Currently slowest adoption. Only water tank TS has been used for low-temperature processes

## Slide 14: Application by sectors: Cold Chain (Transportation)
Commercial readiness of cold chain applications is pretty high.
Could help with developing countries realize off-grid solutions.

## Slide 15: Application by sectors: district & building heating & cooling
Centralized vs individual heating & cooling system
UETS can be deployed at large scales and are commonly used for district heating & cooling.
Thermal batteries for individual buildings to provide flexibility for heat pump adoption.
Currently Water tank ES is widely used across the world

## Slide 16: Barriers to deployment & strategies

## Slide 17: Barriers to deployment & strategies
Identify barriers and actionable for each sector

## Slide 18: Thank you!
For your attention and for many great Fridays in the past 5 years 