## Slide 1
Uranium Mining: From Rocks to Gigawatts
HEJC
Oct 1, 2021
Eric Fell

## Slide 2: Nuclear Power in the U.S.
(2021) US Energy Information Administration
https://www.eia.gov/totalenergy/data/monthly/pdf/mer.pdf
Globally, ~441 nuclear power plants totaling 392 GWe
93 nuclear reactors currently operating in USA (~97 GW)
20% of the nation’s total electric energy generation
Accounts for ~60% of U.S. emission-free energy generation

## Slide 3: Fundamentals of Nuclear Reactions
http://fys246.nuclear.lu.se/topics.asp
All elements have isotopes, large range of stabilities
Radioactive decay occurs in unstable isotopes, resulting in spontaneous emission of particles and/or electromagnetic radiation
Repulsive force between protons must be balanced by a strong attractive force for nuclei stability

## Slide 4: Mass-Energy Equivalence
Energy of nuclear decay comes from mass conversion, on the energy scale of MeV (1.6⨯10-13 J) released for every nuclear reaction

## Slide 5: Fission Reactor TL;DR
Thermal neutrons are captured by fissile fuel
Fuel fissions, releasing fast neutrons and energy
Fast neutrons are slowed by the moderator

## Slide 6: Fission Reactor Classes
Light water reactors
  Pressurized water (PWR)
  Boiling water (BWR)
  RBMK (LWGR)
Heavy Water reactors
  Pressurized heavy water (PHWR or CANDU)
Gas cooled reactors (GCR)
Fast Neutron reactors (FNR)
More than two thirds of the reactors in the world are PWR designs
https://www.world-nuclear.org/our-association/publications/global-trends-reports/world-nuclear-performance-report.aspx

## Slide 7: Fission Reactor Fuel: Uranium-235
  • Naturally occurring but in low abundance (uranium is found >99% as U-238)
  • Can be used in heavy water reactors (unenriched uranium) or light water reactors (enriched uranium)
  • Requires thermal (slow) neutrons for adequate fission, so a moderator is required
  • World’s primary nuclear fissile fuel
 | % U-235
Naturally occurring | 0.7
Reactor grade | 3-5
Weapons grade | 20-85
https://en.wikipedia.org/wiki/Decay_chain
235U Natural decay chain
t1/2 = 7x108 y
Enrichment = ↑% U-235

## Slide 8: Mining Uranium
Average uranium concentration in Earth’s crust is 2.8 ppm (500 times more common than gold)
Most successful mines have ore deposits of >1000 ppm
Uranium can be easily solubilized in ground waters
The main challenge in extracting uranium is finding regions with high enough concentrations to be economically viable
Almost all radioactivity in a uranium ore is from U-238 decay chain
1 kg U = 600,000 kg bananas, in terms of Becquerels (decays/sec)

## Slide 9: Current Uranium Suppliers
https://world-nuclear.org/information-library/nuclear-fuel-cycle/mining-of-uranium/
Current global demand for uranium is 67,000 t/year
Secondary sources (12,000 t/year) come from nuke decommissioning, stockpiles, fuel reprocessing

## Slide 10: Open Pit and Underground Mining
Cigar Lake Mine, Saskatchewan. Opened in 2014, ore body averages 16% U3O8 with proven reserves of 75,000 t
(500 m below surface)
Open pit uranium mine in Namibia
Uranium mining is similar to other forms of mining unless very high ore grades exist, then special techniques used to limit radiation exposure

## Slide 11: In Situ Leaching/Recovery mining (ISL/ISR)
~55% of global mined uranium is from ISL, heavily favored in USA and the ‘stans
Dissolving solutions injected into uranium deposit
More economical for deep, low uranium grade ores
Pumped solution usually contains a mix of oxidant (peroxide/oxygen), complexing agent (sulfuric acid/CO2), and possibly alkali leach based on local rock chemistry
The liquor is then pumped to a uranium recovery plant in the same way as open pit/underground mining

## Slide 12: From Ore to Yellowcake

## Slide 13: From Ore to Yellowcake
Modern yellowcake is not always yellow. Typically, 70-90% U3O8 by weight, with other uranium oxides mixed in
Once uranium-in-liquor is extracted from mining process, it is passed through ion-exchange resins/polymers to separate the U
U3O8 is then precipitated with hydrogen peroxide, and dried
No enrichment has occurred yet. Still @ natural abundances:
99.3% U-238, ~0.7% U-235

## Slide 14: From Yellowcake to Nuclear ____?
Heavy water (CANDU) or RBMK reactors
Majority of nuclear reactors (PWR, BWR)
~20% enriched, fast neutron/research/naval reactors, medical isotope production
>80% enriched, nuclear weapons
Enrichment required

## Slide 15: From Yellowcake to Uranium Hexafluoride
Increased concentration of fissile U-235 required for most nuclear power applications
Yellowcake is first converted to uranium hexafluoride (UF6)
Fluorine has only one naturally-occurring isotope helps with separation
UF6 is a gas at 56 °C
Uranium is now ready for enrichment
Diffusion
Centrifuge

## Slide 16: So You Want to Enrich Uranium?
Diffusion Enrichment
Forcing UF6 gas under high pressure through series of porous membranes
U-235 molecules are slightly lighter, so they move faster through membrane pores
Cascade of many diffusion stages (~1400) leads to 3-4% U-235
Compressors, diffusers, heat exchangers VERY energy-intensive process
Centrifuge Enrichment
UF6 fed into large vacuum tubes with rotors spinning at 50k-70k rpm
Heavier U-238 concentrates at cylinder outer edge
Induced countercurrent flow lets heavier/lighter molecules be siphoned off at cylinder ends
Cascade of 10-20 centrifuge stages, much more energy-efficient than diffusion process
Georges Besse I plant (France), most of nuclear plant's 3.5 GW powered enrichment

## Slide 17: Fuel Rod Formation
3 GWth reactor will consume ~100 tons per year
(Un)enriched UF6 is then chemically processed to UO2 powder
Powder is compressed into pellets, which are then stacked and sealed into fuel rods
Rods are bundled into fuel assembly, 150-300 rods
Typical reactor has 100-200 fuel assemblies
1 t natural uranium
= 120 kg U for reactor fuel
= 6 kg weapons grade
Overall, enrichment accounts for ~half of the cost of nuclear fuel and about 5% of the total cost of the electricity generated

## Slide 18: Global Enrichment Capacity
SWU = separative work unit, amount of separation done by enrichment process
At higher U-235%, less relative effort required for enrichment and so there are many international safeguards in place at enrichment facilities.

## Slide 19: Mixed Oxide (MOX) Fuel
https://www.world-nuclear.org/information-library/nuclear-fuel-cycle/fuel-recycling/mixed-oxide-fuel-mox.aspx
Pu can be recovered from used reactor fuel and mixed with depleted U, forming MOX
MOX fuel provides ~5% of new fuel used today (>10% in France)
Weapons-grade Pu can also be burned up through MOX fuel
Each year about 70 t of plutonium (contained in used fuel) is removed from the world’s reactors

## Slide 20: An Alternative Method: Uranium from Seawater
Uranium concentration in seawater is 3.3 ppb (~1000x less than in Earth’s crust)
However total uranium in oceans is estimated at 4 billion tons (500x land ore-based U)
Concentration does not vary with ocean depth, season, or temperature, and is not taken up by marine organisms
Over 90% of dissolved uranium in seawater is in Ca2[UO2(CO3)3] and Mg[UO2(CO3)3]2− complexes

## Slide 21: Physicochemical Adsorption of Uranium
Most technology for uranium seawater extraction is based on amine polymers sorbents
Many variations to the sorbent chemistry but extraction of the bound uranium is facilitated by changing temperature/pH
Active area of research in designing new ligands that can select U over other trace metal ions in seawater (vanadium, iron, copper etc.)
imidedioximes
amidoximes
Abney, C.W. et al, Chemical Reviews, 2017, 13935-14013

## Slide 22: Uranium from Seawater Program @PNNL
Using amidoxime-based polymer sorbents, adsorption capacities of 5-6 g U/kg sorbent was achieved over 50 days in seawater
Spinout company formed in 2014 based in Idaho, pursuing heavy metals extraction from seawater (was in SBIR phase II as of last year)
Amidoxime polymer ‘braids’
Gill, G.A. et al, Ind. Eng. Chem. Res. 2016, 55, 4264−4277
Did the math: 1 t of sorbent should get you ~40 kg U/year

## Slide 23: More References
Choppin, Liljenzin, Rydberg, Ekberg, Radiochemistry and Nuclear Chemistry
Chart of Nuclides
World Nuclear Association
IEA nuclear
EIA nuclear