## Slide 1: High Altitude Wind
Justin J. Teesdale

## Slide 2: Altitude ≠ Elevation

## Slide 3: Wind Energy: Crude Analysis
50,000 TW transmitted via natural convection
IPCC Fifth Assessment Report, Technical Report
UN World Energy Assessment: 2004 Update
~60 TW ultimately wind kinetic energy near land
~2-6 TW are economically feasible for extraction

## Slide 4: Wind Energy: Crude Analysis
http://gwec.net/global-figures/graphs/
Factoring in a capacity factor of 0.30, we install ~15 GWe per year

## Slide 5: Wind Energy: Crude Analysis
http://gwec.net/global-figures/graphs/
Factoring in a capacity factor of 0.30, we have roughly 161 GWe from wind
At a rate of 15 GWe/yr, we’re on track for wind to account for 641 GWe in 2050
Can we get more wedges?

## Slide 6: Classification of Wind
Most wind turbines access winds in the 5-9 m/s range.
IEEE Trans. Energy Conv. 2007, 22, 136.

## Slide 7: Theoretical Application
Areal Power Density (PA) = 1/2rn3
Highest wind speeds exist in jet streams (~6-11 km above surface)
IEEE Trans. Energy Conv. 2007, 22, 136.

## Slide 8: Theoretical Application
Areal Power Density (PA) = 1/2rn3
Highest wind speeds exist in jet streams (~6-11 km above surface)
IEEE Trans. Energy Conv. 2007, 22, 136.

## Slide 9: Theoretical Application
Areal Power Density (PA) = 1/2rn3
Highest wind speeds exist in jet streams (~6-11 km above surface)
IEEE Trans. Energy Conv. 2007, 22, 136.

## Slide 10: Theoretical Application
Areal Power Density (PA) = 1/2rn3
Highest wind speeds exist in jet streams (~6-11 km above surface)
IEEE Trans. Energy Conv. 2007, 22, 136.
At this altitude, winds are much more consistent, with capacity factors expected to be > 80%.

## Slide 11: Altitude ≠ Elevation
Notes: 20 m/s ~ 45 MPH

## Slide 12: PA = 1/2rn3
http://www.altaeros.com/energy.html

## Slide 13: Directly analogous to wind-surfing. Kinetic energy of kite converted to shaft work at the tether point. “Same power as a wind turbine with 10% of the materials”
Strategy 1: Cheap Kites
http://www.kitegen.com/en/products/stem/

## Slide 14: “Successful test of 3 MW rigging system” Kites typically fly between 800-1000 meters high In March 2017, published the completion of a large scale composites factory to produce kites en masse.
Strategy 1: Status
Largest scale: 300 kW Aircraft typically fly between 100-500 meters high Just started development of autopilot system
Largest scale: 60 kW, 800 m
Design similar to KiteGen. 2018 prototype to test 250 kW. Targeting more dispatchable units.
Plans for a 500 kW setup.
Equity from Shell, Schlumberger among others.

## Slide 15: Generators are mounted to aircraft. Electricity is transmitted through conductive tether.
Strategy 2: Really Expensive Kites
https://x.company/makani/technology/

## Slide 16: Small turbine supported by aerostat. Tested up to 100 m, “rated for 300 m”. $7 million in funding granted in 2017 for research in the BAT, and into telecomm services.
Strategy 2: Status
https://www.greentechmedia.com/articles/read/a-beginners-guide-to-the-airborne-wind-turbine-market#gs.JAUcOic

## Slide 17: Initially, electricity supplied to reach optimal altitude. Once correct amount of lift achieved via wind, crosswinds spin the turbine blades/generator shaft
Makani
https://x.company/makani/technology/

## Slide 18
Makani
https://x.company/makani/technology/
Reported to have received $500 million when acquired by X, but no status reports following acquisition.
No reported data on wind -> electricity efficiency, only generator efficiency (>96%).

## Slide 19
Makani
https://x.company/makani/journey/

## Slide 20
Makani
https://x.company/makani/journey/

## Slide 21
Makani
https://x.company/makani/journey/

## Slide 22
Makani
https://x.company/makani/journey/

## Slide 23
Makani
https://x.company/makani/journey/
https://youtu.be/An8vtD1FDqs

## Slide 24
Makani Gossip
https://www.greentechmedia.com/articles/read/alphabet-remains-committed-to-makani-wind#gs.Kf4WYnI
https://www.bloomberg.com/news/articles/2017-08-04/alphabet-s-green-energy-ambitions-hit-turbulence

## Slide 25
Makani Gossip
https://www.greentechmedia.com/articles/read/alphabet-remains-committed-to-makani-wind#gs.Kf4WYnI
https://www.bloomberg.com/news/articles/2017-08-04/alphabet-s-green-energy-ambitions-hit-turbulence

## Slide 26
High(er) Altitude Wind
https://www.greentechmedia.com/articles/read/alphabet-remains-committed-to-makani-wind#gs.Kf4WYnI
https://www.greentechmedia.com/articles/read/joby-energy-the-tale-of-a-high-flying-entrepreneur#gs.2XGYAbs
These technologies are not really high altitude wind harvesting techs in the way in which it was previously envisioned (<1000 m vs. 10,000+ m).
However, these technologies do provide a nice foundation for actual jet stream technology.

## Slide 27
High(er) Altitude Wind
https://www.greentechmedia.com/articles/read/alphabet-remains-committed-to-makani-wind#gs.Kf4WYnI
https://www.greentechmedia.com/articles/read/joby-energy-the-tale-of-a-high-flying-entrepreneur#gs.2XGYAbs
These technologies are not really high altitude wind harvesting techs in the way in which it was previously envisioned (<1000 m vs. 10,000+ m).
However, these technologies do provide a nice foundation for actual jet stream technology.
Major challenge: transmission of energy from aircraft to tether point. Most startups are already limited by strength, lifetime, drag, and cost of tether materials.

## Slide 28
High(er) Altitude Wind
https://www.greentechmedia.com/articles/read/alphabet-remains-committed-to-makani-wind#gs.Kf4WYnI
https://www.greentechmedia.com/articles/read/joby-energy-the-tale-of-a-high-flying-entrepreneur#gs.2XGYAbs
These technologies are not really high altitude wind harvesting techs in the way in which it was previously envisioned (<1000 m vs. 10,000+ m).
However, these technologies do provide a nice foundation for actual jet stream technology.
Slightly less major challenge: Need dedicated airspace for these devices which limits other air traffic or the location where these devices can be places.
Major challenge: transmission of energy from aircraft to tether point. Most startups are already limited by strength, lifetime, drag, and cost of tether materials.

## Slide 29
High(er) Altitude Wind
https://www.greentechmedia.com/articles/read/alphabet-remains-committed-to-makani-wind#gs.Kf4WYnI
https://www.greentechmedia.com/articles/read/joby-energy-the-tale-of-a-high-flying-entrepreneur#gs.2XGYAbs
These technologies are not really high altitude wind harvesting techs in the way in which it was previously envisioned (<1000 m vs. 10,000+ m).
However, these technologies do provide a nice foundation for actual jet stream technology.
Slightly less major challenge: Need dedicated airspace for these devices which limits other air traffic or the location where these devices can be places.
Major challenge: transmission of energy from aircraft to tether point. Most startups are already limited by strength, lifetime, drag, and cost of tether materials.

## Slide 30
Airborne Wind Generation
https://www.greentechmedia.com/articles/read/alphabet-remains-committed-to-makani-wind#gs.Kf4WYnI
https://www.bloomberg.com/news/articles/2017-08-04/alphabet-s-green-energy-ambitions-hit-turbulence
The field seems to now have branded their tech as airborne wind generators (AWG), with the goal of targeting markets where cost of traditional wind-based energy generation is high.

## Slide 31
Airborne Wind Generation
https://www.greentechmedia.com/articles/read/alphabet-remains-committed-to-makani-wind#gs.Kf4WYnI
https://www.bloomberg.com/news/articles/2017-08-04/alphabet-s-green-energy-ambitions-hit-turbulence
The field seems to now have branded their tech as airborne wind generators (AWG), with the goal of targeting markets where cost of traditional wind-based energy generation is high.
Potential markets:
Unstable/uneven ground such as mountainous regions or offshore sites
https://youtu.be/tx0ugnc5j-g

## Slide 32
Airborne Wind Generation
https://www.greentechmedia.com/articles/read/alphabet-remains-committed-to-makani-wind#gs.Kf4WYnI
https://www.bloomberg.com/news/articles/2017-08-04/alphabet-s-green-energy-ambitions-hit-turbulence
The field seems to now have branded their tech as airborne wind generators (AWG), with the goal of targeting markets where cost of traditional wind-based energy generation is high.
Potential markets:
Unstable/uneven ground such as mountainous regions or offshore sites
Locations where it is cost intensive to have turbine components (tower, turbine blades, etc) shipped/constructed, such as small islands.

## Slide 33
Airborne Wind Generation
https://www.greentechmedia.com/articles/read/alphabet-remains-committed-to-makani-wind#gs.Kf4WYnI
The field seems to now have branded their tech as airborne wind generators (AWG), with the goal of targeting markets where cost of traditional wind-based energy generation is high.
Potential markets:
Unstable/uneven ground such as mountainous regions or offshore sites
Locations where it is cost intensive to have turbine components (tower, turbine blades, etc) shipped/constructed, such as small islands.
Makani is planning to move to Hawaii to test their M600 (600 kW) design in areas closer to populated locations and also potentially to test arrays.