## Slide 1: Industrial Catalysis How Dirt and Sand Catalyze Some of the Most Important Transformations
Justin J. Teesdale
Harvard Energy Journal Club
September 29th, 2017

## Slide 2: Industrial (Petro)Chemical Energy Use
In 2014,
  Total Primary Energy Supply (TPES) = 155,000 TWh (560 EJ)
International Energy Agency (IEA) (2011). Key world energy statistics-2011.
International Energy Agency (IEA) (2007). Tracking Industrial Efficiency and CO2 Emisssions-2007.

## Slide 3: Industrial (Petro)Chemical Energy Use
In 2014,
  Total Primary Energy Supply (TPES) = 155,000 TWh (560 EJ)
Industry uses ~20% of the TPES
International Energy Agency (IEA) (2011). Key world energy statistics-2011.
International Energy Agency (IEA) (2007). Tracking Industrial Efficiency and CO2 Emisssions-2007.

## Slide 4: Industrial (Petro)Chemical Energy Use
In 2014,
  Total Primary Energy Supply (TPES) = 155,000 TWh (560 EJ)
Industry uses ~20% of the TPES
Chemical and Petrochemical (30%)
Iron and Steel (20%)
Non-ferrous metals and minerals (10%)
Paper, pulp, and print (5%)
Food and tobacco
International Energy Agency (IEA) (2011). Key world energy statistics-2011.
International Energy Agency (IEA) (2007). Tracking Industrial Efficiency and CO2 Emisssions-2007.

## Slide 5: Importance of Catalysis in Industry (2004)
International Energy Agency (IEA) (2007). Tracking Industrial Efficiency and CO2 Emisssions-2007.

## Slide 6: Importance of Catalysis in Industry (2004)
International Energy Agency (IEA) (2007). Tracking Industrial Efficiency and CO2 Emisssions-2007.
All products of steam cracking and other high T/high P processes that don’t involve catalysts

## Slide 7: Importance of Catalysis in Industry (2004)
International Energy Agency (IEA) (2007). Tracking Industrial Efficiency and CO2 Emisssions-2007.
All products of steam cracking and other high T/high P processes that don’t involve catalysts
Involves supported metal oxide catalysts

## Slide 8: Importance of Catalysis in Industry (2004)
International Energy Agency (IEA) (2007). Tracking Industrial Efficiency and CO2 Emisssions-2007.
All products of steam cracking and other high T/high P processes that don’t involve catalysts
Involves supported metal oxide catalysts
Methanol and Ammonia production utilizes 1.4 % of TPES

## Slide 9
Steam Reforming of Methane and Water-Gas Shift (WGS)
Haber-Bosch Process
Methanol Production
Fischer-Tropsch Process

## Slide 10: Steam Reforming: Stats
US DOE (2013). Report of the Hydrogen Production Expert Panel.
Responsible for almost 95% of annual production of hydrogen

## Slide 11: Steam Reforming: Stats
US DOE (2013). Report of the Hydrogen Production Expert Panel.
Responsible for almost 95% of annual production of hydrogen
~ 50 million tons of hydrogen produced annually (worldwide)

## Slide 12: Steam Reforming: Stats
US DOE (2013). Report of the Hydrogen Production Expert Panel.
Responsible for almost 95% of annual production of hydrogen
~ 50 million tons of hydrogen produced annually (worldwide)
Primarily used immediately in petroleum industry for the synthesis of other chemicals and ammonia
Largest production of any chemical in industry on a per mole basis by a large margin

## Slide 13: Steam Reforming: The Setup
ECN (2004). On the Catalytic Aspects of Steam-Methane Reforming.

## Slide 14: Steam Reforming: The Setup
ECN (2004). On the Catalytic Aspects of Steam-Methane Reforming.

## Slide 15: Steam Reforming: The Setup
ECN (2004). On the Catalytic Aspects of Steam-Methane Reforming.
Overall process 50-80% efficient, but highly dependent on plant design

## Slide 16: Steam Reforming: Reaction Conditions
ECN (2004). On the Catalytic Aspects of Steam-Methane Reforming.
Mix of steam and methane pass over catalyst @ 700-1000 °C and 3-25 bar
Catalyst typically metal supported on a high surface area material (silica, Al2O3, MgO, etc)

## Slide 17: Steam Reforming: Reaction Conditions
ECN (2004). On the Catalytic Aspects of Steam-Methane Reforming.
Most of this chemistry was developed in 1960s and is still being employed today
Mix of steam and methane pass over catalyst @ 700-1000 °C and 3-25 bar
Catalyst typically metal (nickel) supported on a high surface area material (silica, Al2O3, MgO, etc)

## Slide 18: Steam Reforming: Catalyst Design
Target: New catalysts that can operate at lower temperatures

## Slide 19: Steam Reforming: Catalyst Design
Target: New catalysts that can operate at lower temperatures
Typically employing the same catalyst (Mn/Fe/Co/Ni) but with more sophisticated/expensive supports

## Slide 20: Steam Reforming: Catalyst Design
Target: New catalysts that can operate at lower temperatures
Typically employing the same catalyst (Mn/Fe/Co/Ni) but with more sophisticated/expensive supports
Ni on La2O3–ZrO2–CeO2 support/promoter can go as low as 400 °C

## Slide 21: Steam Reforming: Catalyst Design
Target: New catalysts that can operate at lower temperatures
Typically employing the same catalyst (Mn/Fe/Co/Ni) but with more sophisticated/expensive supports
Ni on La2O3–ZrO2–CeO2 support/promoter can go as low as 400 °C
Preventing catalyst degradation (sintering) via different metal precursors (affects particle size and spacing)

## Slide 22
Steam Reforming of Methane and Water-Gas Shift (WGS)
Haber-Bosch Process
Methanol Production
Fischer-Tropsch Process

## Slide 23: Haber-Bosch: Stats
Responsible for 1-1.5% of annual energy consumption
~ 140 million tons of ammonia produced annually (worldwide)
USGS (2017). Minerals commodity Summaries–Nitrogen (fixed)–Ammonia 2017.
Smil, Vaclav World Agriculture, 2011, 2, 9-13.

## Slide 24: Haber-Bosch: Stats
Responsible for 1-1.5% of annual energy consumption
~ 140 million tons of ammonia produced annually (worldwide)
88% of produced ammonia used for the synthesis of fertilizers
USGS (2017). Minerals commodity Summaries–Nitrogen (fixed)–Ammonia 2017.
Smil, Vaclav World Agriculture, 2011, 2, 9-13.

## Slide 25: Haber-Bosch: Stats
Responsible for 1-1.5% of annual energy consumption
~ 140 million tons of ammonia produced annually (worldwide)
88% of produced ammonia used for the synthesis of fertilizers
Quadrupling of arable land on ice-free continents. At 1900 level production, to produce 2011 quantity of ammonia would require ~50% of total land on ice-free continents (as opposed to 15% now).
USGS (2017). Minerals commodity Summaries–Nitrogen (fixed)–Ammonia 2017.
Smil, Vaclav World Agriculture, 2011, 2, 9-13.

## Slide 26: Haber-Bosch: Stats
Responsible for 1-1.5% of annual energy consumption
~ 140 million tons of ammonia produced annually (worldwide)
88% of produced ammonia used for the synthesis of fertilizers
Quadrupling of arable land on ice-free continents. At 1900 level production, to produce 2011 quantity of ammonia would require ~50% of total land on ice-free continents (as opposed to 15% now).
USGS (2017). Minerals commodity Summaries–Nitrogen (fixed)–Ammonia 2017.
Smil, Vaclav World Agriculture, 2011, 2, 9-13.

## Slide 27: Haber-Bosch: Stats
Quadrelli, E. A. Chem. Soc. Rev. 2014, 43, 547.
Energy-intensive process because N2 is extremely inert

## Slide 28: Haber-Bosch: Stats
Responsible for 1-1.5% of annual energy consumption
~ 140 million tons of ammonia produced annually (worldwide)
88% of produced ammonia used for the synthesis of fertilizers
Quadrupling of arable land on ice-free continents. At 1900 level production, to produce 2011 quantity of ammonia would require ~50% of total land on ice-free continents (as opposed to 15% now).

## Slide 29: Haber-Bosch: The Setup
Notes: 200 atm in catalyst chamber

## Slide 30: Haber-Bosch: The Setup
Haber-Bosch benefitted from 100 years of optimization, as a result efficiencies are typically >95%
Notes: 200 atm in catalyst chamber

## Slide 31: Haber-Bosch: What’s the catch?
DOE Roundtable Report (2016). Sustainable Ammonia Synthesis
Catalyst is simply metallic iron doped with potassium (K2O) and supported on either silica or alumina

## Slide 32: Haber-Bosch: What’s the catch?
The energy intensive components are the heat and pressure necessary in the steam reformer to produce pure H2 to be fed into Haber-Bosch reactor
DOE Roundtable Report (2016). Sustainable Ammonia Synthesis
Catalyst is simply metallic iron doped with potassium (K2O) and supported on either silica or alumina

## Slide 33: Haber-Bosch: What’s the catch?
The energy intensive components are the heat and pressure necessary in the steam reformer to produce pure H2 to be fed into Haber-Bosch reactor
Also heat and pressure necessary for the Haber-Bosch reactor
DOE Roundtable Report (2016). Sustainable Ammonia Synthesis
Catalyst is simply metallic iron doped with potassium (K2O) and supported on either silica or alumina

## Slide 34: Haber-Bosch: What’s the catch?
Catalyst is simply metallic iron doped with potassium (K2O) and supported on either silica or alumina
The energy intensive components are the heat and pressure necessary in the steam reformer to produce pure H2 to be fed into Haber-Bosch reactor
Also heat and pressure necessary for the Haber-Bosch reactor
Significant cost to achieve high purity H2 and N2 as O2, CO, CO2, and other oxygen containing compounds poison the catalyst
DOE Roundtable Report (2016). Sustainable Ammonia Synthesis

## Slide 35: Haber-Bosch: What’s the catch?
The energy intensive components are the heat and pressure necessary in the steam reformer to produce pure H2 to be fed into Haber-Bosch reactor
Also heat and pressure necessary for the Haber-Bosch reactor
Significant cost to achieve high purity H2 and N2 as O2, CO, CO2, and other oxygen containing compounds poison the catalyst
New catalysts must aim to operate at lower temperature and pressure and/or be more selective for N2 conversion to NH3.
DOE Roundtable Report (2016). Sustainable Ammonia Synthesis
Catalyst is simply metallic iron doped with potassium (K2O) and supported on either silica or alumina

## Slide 36: Haber-Bosch: New Catalyst Design
Move towards more sophisticated materials and designs
Fe/K mixtures supported on carbon nanotubes
Extremely high bar set by very cheap materials
Giddey, S. Int. J. Hydrog. Energy, 2013, 38, 14576.

## Slide 37: Haber-Bosch: New Catalyst Design
Jaramillo, T. F. Nat. Mater. 2017, 16, 70.

## Slide 38: Haber-Bosch: New Catalyst Design
Move towards more sophisticated materials and designs
Fe/K mixtures supported on carbon nanotubes
Using ruthenium/activated carbon-based catalysts
Extremely high bar set by very cheap materials
Giddey, S. Int. J. Hydrog. Energy, 2013, 38, 14576.

## Slide 39: Haber-Bosch: New Catalyst Design
Move towards more sophisticated materials and designs
Fe/K mixtures supported on carbon nanotubes
Using ruthenium/activated carbon-based catalysts
Improving steam reforming efficiency or replacing it entirely
Extremely high bar set by very cheap materials
Giddey, S. Int. J. Hydrog. Energy, 2013, 38, 14576.

## Slide 40: Haber-Bosch: New Catalyst Design
Move towards more sophisticated materials and designs
Jaramillo, T. F. Science 2017, 355, 146.
Fe/K mixtures supported on carbon nanotubes
Using ruthenium/activated carbon-based catalysts
Improving steam reforming efficiency or replacing it entirely

## Slide 41: Haber-Bosch: New Catalyst Design
Jaramillo, T. F. Science 2017, 355, 146.

## Slide 42
Steam Reforming of Methane and Water-Gas Shift (WGS)
Haber-Bosch Process
Methanol Production
Fischer-Tropsch Process

## Slide 43: Methanol: Stats
40% of methanol is converted to formaldehyde
International Energy Agency (IEA) (2007). Tracking Industrial Efficiency and CO2 Emisssions-2007.

## Slide 44: Methanol: Stats
40% of methanol is converted to formaldehyde
Remaining methanol is used in the synthesis of fine chemicals or as a fuel additive
International Energy Agency (IEA) (2007). Tracking Industrial Efficiency and CO2 Emisssions-2007.

## Slide 45: Methanol: Stats
40% of methanol is converted to formaldehyde
Remaining methanol is used in the synthesis of fine chemicals or as a fuel additive
Responsible for ~0.4 % of world energy use
International Energy Agency (IEA) (2007). Tracking Industrial Efficiency and CO2 Emisssions-2007.

## Slide 46: Methanol: Catalyst
Industrial catalyst is an alumina pellet (Al2O3) coated in copper/zinc oxides
Catalyst is >99.5% efficient (not overall energy efficiency)
http://www.technology.matthey.com/article/61/3/172-182/

## Slide 47: Methanol: Catalyst
Industrial catalyst is an alumina pellet (Al2O3) coated in copper/zinc oxides
Catalyst is >99.5% efficient (not overall energy efficiency)
Requires temperatures 400-600 °C and pressures of 40-100 atm.
http://www.technology.matthey.com/article/61/3/172-182/
Energy efficiency and cost is gated by steam reformation (H2)

## Slide 48: Methanol: Catalyst
Industrial catalyst is an alumina pellet (Al2O3) coated in copper/zinc oxides
Catalyst is >99.5% efficient (not overall energy efficiency)
Requires temperatures 400-600 °C and pressures of 40-100 atm.
http://www.technology.matthey.com/article/61/3/172-182/
Same catalyst that was first used in 1960s
Energy efficiency and cost is gated by steam reformation (H2)

## Slide 49: Methanol: Catalyst Design
Develop catalysts that operate at lower T and P or
come up with a new system entirely
Norskov, J. K. Nat. Chem. 2014, 6, 320.
Jaramillo, T. F. 2017, 5, 955.
Jaramillo, T. F. 2014, 136, 14107.

## Slide 50: Methanol: Catalyst Design
Develop catalysts that operate at lower T and P or
come up with a new system entirely
Norskov, J. K. Nat. Chem. 2014, 6, 320.
Jaramillo, T. F. 2017, 5, 955.
Jaramillo, T. F. 2014, 136, 14107.

## Slide 51: Methanol: Catalyst Design
Develop catalysts that operate at lower T and P or
come up with a new system entirely
Norskov, J. K. Nat. Chem. 2014, 6, 320.
Jaramillo, T. F. 2017, 5, 955.
Jaramillo, T. F. 2014, 136, 14107.

## Slide 52: Methanol: Catalyst Design
Develop catalysts that operate at lower T and P or
come up with a new system entirely
Norskov, J. K. Nat. Chem. 2014, 6, 320.
Jaramillo, T. F. 2017, 5, 955.
Jaramillo, T. F. 2014, 136, 14107.

## Slide 53
Steam Reforming of Methane and Water-Gas Shift (WGS)
Haber-Bosch Process
Methanol Production
Fischer-Tropsch Process

## Slide 54: Fischer-Tropsch: Stats
Discovered in 1925 by Franz Fischer and Hans Tropsch
Syngas heated over a catalyst bed (typically Fe or Co) at 25 atm and either 230 °C (LTFT) or 320 °C (HTFT)
Klerk, A. Green Chem. 2008, 10, 1249.

## Slide 55: Fischer-Tropsch: Stats
Discovered in 1925 by Franz Fischer and Hans Tropsch
Syngas heated over a catalyst bed (typically Fe or Co) at 25 atm and either 230 °C (LTFT) or 320 °C (HTFT)
Klerk, A. Green Chem. 2008, 10, 1249.

## Slide 56: Fischer-Tropsch: Stats
Viability heavily depends on crude oil prices, as a result, there are very few plants in operation
Klerk, A. Green Chem. 2008, 10, 1249.

## Slide 57: Fischer-Tropsch: Stats
Viability heavily depends on crude oil prices, as a result, there are very few plants in operation
Klerk, A. Green Chem. 2008, 10, 1249.
South African company that does coal-to-liquids
Gas-to-liquids (GTL) facility in Malaysia
X-to-liquids (XTL) facility in Australia

## Slide 58: Fischer-Tropsch: Stats
Viability heavily depends on crude oil prices, as a result, there are very few plants in operation
Klerk, A. Green Chem. 2008, 10, 1249.
Also challenging due to significantly less data
Difficult to pin down overall energy efficiency due to variability in plant design and catalyst employed
South African company that does coal-to-liquids
Gas-to-liquids (GTL) facility in Malaysia
X-to-liquids (XTL) facility in Australia

## Slide 59: Fischer-Tropsch: Why we care
Provides security in gasoline/diesel sector
Requires a supply of syngas which can be generated from multiple sources
http://www.syngaschem.com/

## Slide 60: Fischer-Tropsch: Catalyst Design
Very similar to catalysts developed for methanol production
The low selectivity catalysts are typically sold as FT catalysts

## Slide 61: Fischer-Tropsch: Catalyst Design
Very similar to catalysts developed for methanol production
The low selectivity catalysts are typically sold as FT catalysts
Big area of research in industry (Chevron)
…..and also in academia

## Slide 62: Fischer-Tropsch: Catalyst Design
Navarro, V. Nat. Chem. 2016, 8, 929.

## Slide 63
Jiao, F.; Li, J.; Pan, X. Science 2016, 351, 1065.

## Slide 64: Summary and Outlook
Steam Reforming of Methane and Water-Gas Shift (WGS)
Haber-Bosch Process
Methanol Production
Fischer-Tropsch Process

## Slide 65: Summary and Outlook
Steam Reforming of Methane and Water-Gas Shift (WGS)
Haber-Bosch Process
Methanol Production
Fischer-Tropsch Process
Major Challenges
Efficiency improvements or new method for H2
Better catalysts for Haber-Bosch and Fischer-Tropsch (syngas generation)

## Slide 66: Summary and Outlook
Steam Reforming of Methane and Water-Gas Shift (WGS)
Haber-Bosch Process
Methanol Production
Fischer-Tropsch Process
Major Challenges
Efficiency improvements or new method for H2
Better catalysts for Haber-Bosch and Fischer-Tropsch (syngas generation)
How do we do these processes as we move away from fossil fuels?