## Slide 1: Industrial Sector End-Use Energy
HEJC December 3rd, 2015
Lauren Kuntz

## Slide 2
Notes: Create all the physical products in our lives
30% of global emissions (40% if don’t count land-use) -> Mostly due to material processing (turning resources (oil, ore, biomass)/scrap into useful materials
Industry mainly construction, food are the services they provide, emissions largely just 3 categories: burners, process, machines
70% of total final energy use is fossil fuels in industry, but distribution widely dependent on sector

## Slide 3
Notes: Growth of Production in different industries
Part of huge increase due to urbanization (need to build) and globalization of industry – can trade more easily throughout the production process
Over 80% of increase in production since 1990 from China, India, and other developing Asian nations

## Slide 4: Top Producers of Energy Intensive Industrial Goods
Iron Ore | 
China | 43%
Australia | 18%
Brazil | 13%
Steel | 
China | 48%
Japan | 7%
US | 6%
Cement | 
China | 63%
India | 7%
US | 2%
Ammonia | 
China | 32%
India | 9%
Russia | 7%
Notes: Almost all steel produced in China used in mainland china (46% of global steel use, 48% of production)

## Slide 5: Emissions (13.14 GtCO2)
Direct - 5.27 GtCO2
Process – 2.59 GtCO2
Indirect – 5.25 GtCO2
Chart: 
| cement | chemicals | lime | coke ovens | non-ferrous metals | iron/steel | ferroalloy | lime-stone/dolomite | other
 | 1.352 | 0.477 | 0.242 | 0.134 | 0.074 | 0.072 | 0.061 | 0.06 | 0.115
Process Emissions Breakdown
Notes: Indirect = Electricity + Heat

## Slide 6: Direct and Process CO2 Emissions
Notes: Iron and Steel, Cement, and Chemicals make up nearly ¾ of emissions

## Slide 7
Notes: Growth in Emissions largely driven from Asian

## Slide 8: General Emission Reduction Strategies
Notes: Energy Efficiency (Energy use = drive chemical reactions, create heat, mechanical work; thermo limits, but can improve)
Emissions Efficiency (Fuel switching, CCS)
A. Material Efficiency in Manufacturing (reducing losses in stamping/shaping, reusing old material)
B. Material Efficiency in Product Design (may products could be 1/3 lighter without loss of performance, substitution – hard due to levels of material needed)
Product-Service Efficiency (car sharing, higher building occupancy, food waste)
Service Demand Sector (use less things)
After that – Waste Industry Recycle, Re-Use, or Discard (avoids need to create material from scratch – a lot less energy. Not always enough, and not always the best quality)

## Slide 9: General Emission Reduction Challenges
Capital Stock Turnover Time
Global Market Structure
Limited Knowledge Sharing
Energy Subsidies
Notes: Using best available technology in the 5 biggest energy sectors in industry (chemicals, iron/steel, cement, pulp/paper, and aluminium) would reduce industrial energy use by 13% (emissions by 12%)

## Slide 10: Iron and Steel
Notes: Fe2O3 (Ironore) + 3CO (from coke) -> 3CO2 + 2 Fe (Pure Iron)

## Slide 11: Iron and Steel - Technological Options
Dominant Technologies
  Blast Furnace/Basic Oxygen Furnace (13-14 GJ/tonne)
  Scrap/Electric Arc Furnace (4-6 GJ/tonne)
New Technology Options
  Direct Iron Reduction
  Smelting Reduction
  Coke Replacement with Charcoal or Waste Plastic
  Carbon Capture and Sequestration
Notes: Coal based DRI – remove need for coke (but need more coal, and energy efficiency depends on use of reuse of residual gas)
Natural Gas based DRI – Natural gas made into H2 and CO
DRI needs more electricity for EAC
Smelting reduction – much reduction takes place in a liquid iron bath (can use low quality coal instead of coke – save energy/emissions from coking process)

## Slide 12: Iron and Steel - Material Flow
Notes: Availability + Recycling Rate – 26% is lost as process scrap (eliminating this would reduce emissions 16% for the iron/steel sector)
Better materials (allow for less to be used – although not always the case with cars)
30% of all steel produced in 2008 could be re-used in the future, but steel is cheaper than labor (amplified by tax policies) – economically drives material inefficiency to minimize labor costs
Commercial buildings in developed world built with 2x steel required by safety codes.
Extending building life would also help

## Slide 13: Cement
Notes: Much lower energy intensity per tonne than steel and aluminum, but volume of production is much higher – demand dominated by construction
Limestone, clay, sand = feedstock (give lime, silica, alumina, and iron) -> clinker; add gypsum and grind for cement

## Slide 14: Cement
Notes: Heat with coal, natural gas, oil to temperatures of 2000 C
Calcination: CaCO3 -> CaO + CO2 (limestone -> lime + carbon dioxide)
Adding preheaters and precalciners can increase efficiency substantially

## Slide 15: Cement – Technological Options
Notes: Thermodynamic limit of minimum energy: 1.8 GJ/t clinker for dry limestone feedstock
Emissions highly dependent of system and fuel used

## Slide 16: Cement – Technological Options
Notes: Thermodynamic limit of minimum energy: 1.8 GJ/t clinker for dry limestone feedstock
Using best available technology could save 21% of energy consumption – although need to rebuild (can’t easily retrofit) and plant lasts 50 years
In US, half of plants built since 1980, 22% in 70s, 16% in 60s, 10% before 60s

## Slide 17: Cement – Technological Options
Notes: Capital stock in Europe new that US, less room for improvement

## Slide 18: Cement – Technological Options
Clinker Substitute
  Fly-Ash
  Blast Furnace Slag
  Pozzolana
Fuel Substitution
Cement Alternatives
Carbon Capture and Sequestration
Notes: Availability for blending limited (also can’t have long distance transport)
Waste fuels (clinker/limestone act as gas cleaning agents) – tires, wood, plastics, chemicals, municipal solid waste
Some plants have 100% substitution
Hard to recycle/reuse – best to expand building life

## Slide 19: Chemicals
Largest energy user in industrial sector – 10% of global energy use, 7% of global CO2 emissions
Emissions dominated by:
  Ethylene
  Ammonia
  Nitric Acid
  Adipic Acid and Caprolactam (used in plastics)
  Fertilizer
  Synthetic Fibers

## Slide 20: Chemicals – Technological Options
Process integration and process intensification
Combined heat and power
Membranes
Bio-based Chemicals/Plastics
Carbon Capture and Storage
Notes: Integration/intensification – using waste heat, using by-products more efficiently
CHP faces barriers: emission limits/tax rates and feed-in tariffs
Bio-based: use natural polymers, use monomers, and polymerize them, produce from micro-organisms
Plant lifetime = 60 years, average age of capital stock in Europe/N America ~20 years, China ~ 10 years

## Slide 21: Waste Management
Notes: Energy Recovery from Waste – MSW largely biogenic/petrochemical compounds are C and H; mostly combusted on moving grate; need to pay attention to air pollution
Landfill Methane Recovery – of methane generated only 10% captured at sanitary landfills (capture efficiencies only about 50%, up to 95% possible)
Landfill Aeration – introduce ambient air to promote biological processes to limit methane release